## Slide 1: Self-Driving Hardware and Software Architectures
Module 2

## Slide 2: In this module ...
Sensors for perception
Self-driving computing hardware
Designing hardware configurations（レイアウト）
Software architecture, decomposition
Environment representation for self-driving（マップ）
2

## Slide 3
Course 1, Module 2, Lesson 1
Sensors and Computing Hardware

## Slide 4: Sensors
4
Sensor: 環境のプロパティ/その変化を計測/検知するデバイス(device that measures or detects a property of the environment, or changes to a property)
Categorization:
o exteroceptive（外受容）: extero = surroundings
o proprioceptive（自己受容、固有受容）: proprio = internal

## Slide 5: Sensors for perception
Essential for correctly perceiving environment
Comparison metrics:
  Resolution
  Field of view
  Dynamic range（画像の一番明るい色調と一番暗い色調の差（同じ色）、高いdynamic rangeは夜の運転に大事）
Trade-off between resolution and FOV?
Camera
exteroceptive
Dynamic range: the difference between the darkest and the lightest tones（色調、しきちょう） in an image. High dynamic range is critical for self-driving vehicles due to the highly variable lighting conditions encountered while driving especially at night.
- A tone is one of the lighter, darker, or brighter shades of the same color
- A shade of a particular color is one of its different forms. For example, emerald green and olive green are shades of green.
広いFOVは、視野を広げるが、あるオブジェクトのピクセル数が減る
Wider field of view permits a larger viewing region in the environment. But fewer pixels that absorb light from one particular object.
Camera: passive（受動的）, light-collecting sensor
Resolution : the number of pixels that create the image.
Field of View: the horizontal and vertical angular extent that is visible to the camera, and can be varied through lens selection and zoom.

## Slide 6: Sensors for perception
Enables depth estimation from image data
  視差マップを利用する。コース３で紹介
exteroceptive
Stereo
Left and right images
The combination of two cameras with overlapping fields of view and aligned image planes. depth estimation from synchronized image pairs.
Pixel values from image can be matched to the other image producing a disparity map（視差マップ） of the scene.
This disparity can then be used to estimate depth at each pixel.

## Slide 7: Sensors for perception
Detailed 3D scene geometry from LIDAR point cloud
Comparison metrics:
  Number of beams
  Points per second
  Rotation rate
  Field of view
  Detection range (the power output of the light source)
Upcoming: Solid state LIDAR!
LIDAR
exteroceptive
(it can collect) (the more detailed the 3D point cloud can be)
shooting light beams into the environment and measuring the reflected return. measuring the amount of returned light and time of flight of the beam.
a spinning element with multiple stacked light sources
8, 16, 32, 64
(the faster the 3D point clouds are updated)
なぜLiDARが必要？LiDARも光、Cameraも光 。
- LiDAR output a three dimensional point cloud map, which is great for assessing scene geometry.
- Because it is an active（アクティブ） sensor with its own light sources, LiDAR are not affected by the environment’s lighting. So LiDAR do not face the same challenges as cameras when operating in poor or variable lighting conditions.
最新LIDAR：High-resolution, solid-state LIDAR, No rotational component；
安い：the future of affordable self-driving

## Slide 8: Sensors for perception
RADAR
Robust Object Detection and Relative Speed Estimation
Comparison metrics:
o range
o field of view
o position and speed accuracy
Configurations:
  WFOV, short range
  NFOV, long range
Works in poor visibility（可視性） like fog and precipitation!
exteroceptive

## Slide 9: Sensors for perception （超音波、ちょうおんぱ）
Ultrasonics
Short-range all-weather distance measurement
Ideal for low-cost parking solutions
Unaffected by lighting, precipitation
Comparison metrics:
  Range
  Field of view
  Cost
exteroceptive

## Slide 10: proprioceptive
Sensors for perception
Global Navigation Satellite Systems and Inertial measurement units（慣性計測装置）
Direct measure of ego vehicle states
o position, velocity (GNSS)
Varying accuracies: RTK, PPP, DGPS
o angular rotation rate (IMU)
o acceleration (IMU)
o heading (IMU, GPS)
GNSS/IMU
GPS or Galileo

## Slide 11: proprioceptive
Sensors needed for perception（オドメトリ）
Tracks wheel velocities and orientation
Uses these to calculate overall speed and orientation of car
o speed accuracy
o position drift
Wheel Odometry

## Slide 12: Sensors needed for perception: Summary
Camera
LIDAR
RADAR
Ultrasonics
GNSS/IMU
Wheel Odometry

## Slide 13: Sensors needed for perception
GNSS antenna
Ultrasonics
Central Wheel OdometrCy omputer
LIDAR
Cameras
Radar

## Slide 14: Computing Hardware
Need a “self-driving brain”
  Takes in all sensor data
  Computes actions
  Already existing advanced systems that do self driving car processing (e.g. Drive PX/AGX(multiple GPUs), Intel & Mobileye EyeQ)
(have FPGAs to accelerate parallelizable compute tasks)

## Slide 15: Computing Hardware
Need a “self-driving brain”
Image processing, Object detection, Mapping
  GPUs - Graphic Processing Unit
  FPGAs - Field Programmable Gate Array
    製造後に購入者や設計者が構成を設定できる集積回路であり、広義にはPLD（プログラマブルロジックデバイス）の一種である
  ASICs - Application Specific Integrated Chip（特定用途向け集積回路）
    特定の用途向けに複数機能の回路を1つにまとめた集積回路の総称である
だからAny computing brain for self-driving needs both serial（シリアル） and parallel compute modules.

## Slide 16: Computing Hardware
Need a “self-driving brain”
Image processing, Object detection, Mapping
  GPUs, FPGAs, ASICs
Synchronization Hardware
  To synchronize different modules and provide a common clock（センサーフュージョンに重要）
GPS relies on extremely accurate timing to function, and as such can act as an appropriate reference clock when available. （GPSが基準クロックになるが、GPSは使えない時もあるので、同期ハードウェアが必要）
sensor measurements must be timestamped with consistent times for sensor fusion to function correctly.（センサーの間の同期）

## Slide 17: Summary
Sensors - exteroceptive and proprioceptive
o camera, LIDAR, RADAR, ultrasonics, GNSS, IMU, wheel odometry
Self-driving computing hardware
17
More about sensors and computing software: http://wavelab.uwaterloo.ca/sharedata/ME597/ME597_Lecture_Slides/ME597-4- Measurement.pdf

## Slide 18: Hardware Configuration Design
Module 2, Lesson 2

## Slide 19: Sensors
Camera
LIDAR
RADAR
Ultrasonics
GNSS/IMU
Wheel Odometry
Sensors:
camera for appearance input,
stereo camera for depth information,
lidar for all whether 3D input,
radar for object detection,
ultrasonic for short-range 3D input,
GNSS/IMU data and wheel odometry for ego state estimation.

## Slide 20: Assumptions
Aggressive deceleration =
Comfortable deceleration =
o This is the norm, unless otherwise stated
Stopping distance:
reasonably comfortable while still allowing the car to come to a stop quickly
自乗、じじょう

## Slide 21: Where to place sensors?
Need sensors to support maneuvers within our ODD
Broadly, we have two driving environments
 | Highway | Urban（都市） / Residential（住宅）
Traffic Speed | High | Low - Medium
Traffic Volume | High | Medium - High
# of lanes | More | 2-4 typically
Other Features | Fewer, gradual curves; merges | Many turns and intersections

## Slide 22: Highway Analysis
Broadly, 3 kinds of maneuvers:
Emergency Stop
Maintain Speed
Lane Change

## Slide 23: Highway Analysis: Emergency Stop
If there is a blockage ahead, we want to stop in time.
Longitudinal Coverage:
Assume we are speeding at 120 kmph.
Stopping distance could be
~110 metres; aggressive deceleration
なのでMost self-driving systems aim for sensing ranges of 150 ~ 200m in front of the vehicle as a result.
この図によると、大きいFOVのセンサーをしている。なぜ大きいFOVが必要かまだ分かっていない

## Slide 24: Highway Analysis: Emergency Stop
To avoid collision, either we stop or change lanes.
Lateral Coverage:
At least adjacent lanes, since we may change lanes to avoid a hard stop.

## Slide 25: Highway Analysis: Maintain Speed
Relative speeds are typically less than 30 kmph.
Longitudinal coverage:
At least ~100 metres in front.
Both vehicles are moving, so don’t need to look as far as emergency-stop case.（この文は誤解させそうです。講師も言っていない。この文は、maintain speedのために使ったセンサーの検知距離は、emergency stopのセンサーより短いと言ってるようです。でも「overall coverage, slide 32」スライドでは逆に見えてる。個人的には、ここで検知距離より、FOVから考えたほうが理解しやすい。Maintain speedで自車線の前走車しか見る必要がないので、FOVは小さい。FOVが小さいセンサーの検知距離は長いのではないかと思っている。）

## Slide 26: Highway Analysis: Maintain speed with Merge
Lateral Coverage:
Usually current lane
Adjacent lanes would be preferred for merging vehicle detection.
Laterally: A wide 160 to 180 degree field of view is required to track adjacent lanes and a range of 40 ~ 60m is needed to find space between vehicles.

## Slide 27: Highway Analysis: Lane Change
Longitudinal coverage: Need to look forward to maintain a safe distance.
Need to look behind to see what rear vehicles are doing.

## Slide 28: Highway Analysis: Lane Change
Laterally, we need to look not just in the adjacent lanes, but probably further.
Lateral coverage: Need wider sensing
what if?
what if a vehicle attempts to maneuver into the adjacent lane at the same time as we do?
The sensor requirements for lane changes are roughly equivalent to those in the maintain speed scenario.

## Slide 29: Highway Analysis: Overall Coverage
Emergency Stop
Emergency Stop, Maintain Speed
Maintain Speed, Lane Change
Lane Change

## Slide 30: Urban Analysis
Broadly, 6 kinds of maneuvers:
Emergency Stop
Maintain Speed
Lane Change
Overtaking（追い越し）
Turning, crossing at intersections
Passing roundabouts(ラウンドアバウト、環状交差点)

## Slide 31: Urban Analysis
Similar to highway analysis!
Broadly, 6 kinds of maneuvers:
Emergency Stop
Maintain Speed
Lane Change
Overtaking
Turning, crossing at intersections
Passing roundabouts

## Slide 32: Urban Analysis: Overtaking
Longitudinal coverage:
If overtaking a parked（駐車中） or moving vehicle, need to detect oncoming traffic beyond point of return to own lane（自車レーンに戻る点より遠くの対向車を検知）.
wide short-range sensors to detect the parked car.
narrow long-range sensors to identify if oncoming traffic is approaching.

## Slide 33: Urban Analysis: Overtaking
Lateral coverage:
Always need to observe adjacent lanes.
Need to observe additional lanes if other vehicles can move into adjacent lanes.

## Slide 34: Urban Analysis: Intersections
Observe beyond intersection for approaching vehicles, pedestrian crossings, clear exit lanes.
Requires near omni- directional(全方向) sensing for arbitrary intersection angle
s.

## Slide 35: Urban Analysis: Roundabouts
Lateral coverage:
Vehicles are slower than usual, limited range requirement.
Longitudinal coverage:
Due to the shape of the roundabout, need a wider field of view.
wide-range, short distance sensor laterally since the traffic is slow.
wide-range, short distance sensor longitudinally because of how movement around the roundabout occurs.

## Slide 36: Urban Analysis: Overall Coverage
Emergency Stop, Overtaking
Emergency Stop, Maintain Speed, Lane Change, Overtaking, Intersections,
Roundabouts
Overtaking, Intersections Overtaking, Intersections Roundabouts

## Slide 37: Overall Coverage & Sensors Analysis
Short range (ultrasonics)
Long range
Medium range
The need for full 360 degrees sensor coverage on the short scale out to about 50m. And much longer range requirements in the longitudinal direction.

## Slide 38: Summary
Sensor coverage analysis - longitudinal and lateral coverage
o highway driving
o urban driving
23
More about sensing requirements for automated vehicles for highway and rural environments:
[2014] Sensing requirements for an automated vehicle for highway and rural environments.
https:// repository.tudelft.nl/ islandora/object/ uuid:2ae44ea2- e5e9-455c-8481-8284f8494e4e
K.J. Bussemaker’s master’s thesis.

## Slide 39
Course 1, Module 2, Lesson 3
Software Architecture
1

## Slide 40: Software Architecture | High-level
Motion Planning
Environment Perception
Environment Mapping
System Supervisor
Controller
Sensors Output
Actuation
The raw sensor measurements are passed into two sets of modules (Environment perception & mapping) dedicated to understanding the environment around the car.
The environment mapping module creates a set of maps which locate objects in the environment around the autonomous vehicle for a range of different uses, from collision avoidance to egomotion tracking and motion planning.
Motion Planningのmainアウトプット：a safe, efficient and comfortable planned path.
The Controller module takes the path and decides on the best steering angle, throttle position, brake pedal position, and gear settings to precisely follow the planned path.
The System Supervisor is also responsible for informing the safety driver of any problems found in the system.

## Slide 41: Software Architecture | Environment Perception
Localization
GPS / IMU / Wheel Odometry
Vehicle Position
Dynamic Object Detection
Bounding Boxes
Static Object Detection
Dynamic Object Tracking
Inputs
Static Objects
Object Motion Prediction
HD Road Map
Dynamic Objects
LIDAR
Cameras Radar
Object Tracks
Environment Mapping
System Supervisor
タスク：
- identifying the current location of the autonomous vehicle in space
- classifying and locating important elements of the environment for the driving task.
Sensors Output
Environment Perception
Motion Planning
予測の仕事はObject Motion Predictionに属する だろう。 Localizationの仕事は？ Dynamic Object Detection, Dynamic Object Tracking, Static Object Detectionの仕事はある？

## Slide 42: Software Architecture | Environmental Maps
Environment Mapping
System Supervisor
Occupancy Grid Map
LIDAR
Object tracks
Detailed Road Map
Prior Road Map
Vehicle Position Segmented Image
Static Objects
Occupancy Grid Map（occupancy gridは走行できない場所）
Detailed Road Map
Localization Map
Localization Map
Sensors Output
Environment Perception
Motion Planning
Occupancy Grid Map, Localization Map, Detailed Road Mapの仕事は今どうなっている？
Environment PerceptionとEnvironment Mapping のinteraction
For example, the perception module provides the static environment information needed to update the detailed road map, which is then used by the prediction module to create more accurate dynamic object predictions.

## Slide 43: Software Architecture | Environmental Maps
Occupancy Grid Map
LIDAR
Object tracks
Detailed Road Map
Prior Road Map
Vehicle Position Segmented Image
Static Objects
Occupancy Grid Map
Detailed Road Map
Localization Map
Localization Map
Environment Mapping
System Supervisor
Sensors Output
Environment Perception
Motion Planning
Occupancy（占有、せんゆう） Grid Map
- a map of all static objects in the environment surrounding the vehicle (メインLIDAR)
- Filtering LIDAR: the drivable surface（路⾯） points and dynamic object points are removed.
- a set of grid cells and probability that each cell is occupied.

## Slide 44: Software Architecture | Environmental Maps
Environment Mapping
System Supervisor
Occupancy Grid Map
LIDAR
Object tracks
Detailed Road Map
Prior Road Map
Vehicle Position Segmented Image
Static Objects
Occupancy Grid Map
Detailed Road Map
Localization Map
Localization Map
Sensors Output
Environment Perception
Motion Planning
Localization Map (LIDAR & Camera)
センサーデータは、Localization mapと比較して、自車のモーション（移動量）を決める。
このモーションを、GPS, IMUと一緒に自車をlocalizeする。
Sensor data is compared to this map while driving to determine the motion of the car relative to the localization map.
This motion is then combined with other proprioceptor sensor information to accurately localize the ego vehicle.

## Slide 45: Software Architecture | Environmental Maps
Environment Mapping
System Supervisor
Occupancy Grid Map
LIDAR
Object tracks
Detailed Road Map
Prior Road Map
Vehicle Position Segmented Image
Static Objects
Occupancy Grid Map
Detailed Road Map
Localization Map
Localization Map
Sensors Output
Environment Perception
Motion Planning
Detailed Road Map（HDマップ+静的オブジェ クト）
- road segments, signs and lane markings
- a combination of prerecorded data as well as incoming information from the current static environment gathered by the perception stack (Environment Perception)

## Slide 46: Software Architecture | Motion Planning
Mission Planner
Behavior Planner
Local Planner
Current Goal Detailed Road Map Vehicle Position
Mission Path
Behavior Constraints
Planned Trajectory
Dynamic Objects
Vehicle Position Dynamic Objects
Occupancy Grid
Environment Mapping
System Supervisor
the optimal sequence of road segments that connect your origin and destination, Behavior Plannerが使う
Sensors Output
Environment Perception
Motion Planning
long term planning
short term planning
output:
Decisions (例えば、whether the vehicle should merge into an adjacent lane given the desired speed and the predicted behaviors of nearby vehicles.),
Constraints (例えば、 how long to remain in the current lane before switching)
immediate or reactive planning
a specific path and velocity profile. smooth, safe, and efficient given all the current constraints.
Mission Planner, Behavior Planner, Local Plannerは全部ある？

## Slide 47: Software Architecture | Motion Planning
6
11
Local Planner
Behavior Constraints
Planned Trajectory
Current Goal Detailed Road Map | Mission Planner |  | 7 | 4 1 8 |  |  |  |  | 
Vehicle Position Dynamic Objects | Mission Path Behavior Planner | 7 1 | 2 1 6 9 3 | 2 13 5 8 9 7 8 | 9 | 1 2 | 1 2 9 | 4 | 0
Vehicle Position Dynamic Objects
Occupancy Grid
Environment Mapping
System Supervisor
Sensors Output
Environment Perception
Motion Planning
ダイクストラ（Dijkstra）法などコース4で紹介

## Slide 48: Software Architecture | Motion Planning
Mission Planner
Behavior Planner
Local Planner
Current Goal Detailed Road Map Vehicle Position
Mission Path
Behavior Constraints
Planned Trajectory
Dynamic Objects
Vehicle Position Dynamic Objects
Occupancy Grid
Environment Mapping
System Supervisor
Sensors Output
Environment Perception
Motion Planning

## Slide 49: Software Architecture | Motion Planning
Mission Planner
Behavior Planner
Local Planner
Current Goal Detailed Road Map Vehicle Position
Mission Path
Behavior Constraints
Planned Trajectory
Dynamic Objects
Vehicle Position Dynamic Objects
Occupancy Grid
Environment Mapping
System Supervisor
Sensors Output
Environment Perception
Motion Planning
Conformal Lattice（格子） Planning、コース4で紹介

## Slide 50: Software Architecture | Vehicle Controller
Steering Controller
Steering Angle
Planned Trajectory
Vehicle Position
Velocity Controller
Throttle percentage
Brake percentage
Environment Mapping
System Supervisor
Both controllers calculate current errors and tracking performance of the local plan, and adjust the current actuation commands to minimize the errors going forward.つまりできるだけ local planner のplanned trajectoryに沿って進 むように
Sensors Output
Environment Perception
Motion Planning

## Slide 51: Software Architecture | System Supervisor
Motion Planning
Environment Perception
Environment Mapping
Controller
Sensor Outputs
Software Supervisor
Hardware Supervisor
Environment Mapping
System Supervisor
analyzing inconsistencies between the outputs of all modules
Sensors Output
Environment Perception
Motion Planning
Hardware supervisor
1. hardware faults: a broken sensor, a missing measurement, degraded（劣化した） information.
2. analyze the hardware outputs for any outputs which do not match the domain which the self-driving car was programmed to perform under. ( 例 え ば 、 if one of the camera sensors is blocked by a paper bag or if snow is falling and corrupting the LIDAR point cloud data.) まだODD内か？

## Slide 52: Summary
Describe the basic architecture of a self-driving software system
  Environment Perception
  Environment Mapping
  Motion Planning
  Controller
  System Supervisor
Next: Closer look at Environment Mapping
More about AV software architecture: [2007] DAPRA Challenge Technical Paper: https://pdfs.semanticscholar.org/c10a/cd8c64790f7d040ea6f01d7b26b1d9a442db.pdf

## Slide 53: Environment Representation
JULY 28, 2018
PREPARED BY MARKO ILIEVSKI

## Slide 54: Environmental Map Types
Localization of vehicle in the environment.
  Localization point cloud or feature map.
Collision avoidance with static objects.
  Occupancy grid map.
Path planning.
  Detailed road map.
feature map、つまりカメラを使う場合
- detailed positions for all regulatory elements, regulatory attributes（ 例 え ば right turn markings or crosswalks） and lane markings

## Slide 55: Point cloud or Feature Map (Localization Map)
Collects continuous sets if LIDAR
The difference between LIDAR maps is used to calculate the movement of the autonomous vehicle
- created using a continuous set of LIDAR points or camera image features
- used in combination with GPS, IMU and wheel odometry by the localization module to accurately estimate the precise location of the vehicle at all times
- The localization map can be quite large, and many methods exist to compress its contents and keep only those features that are needed for localization.
ORB_SLAMもfeature mapの場合の１つだろう

## Slide 56: Occupancy Grid
Discretized fine grain grid map
  Can be 2D or 3D
Occupancy by a static object
  Trees and buildings
Curbs and other non drivable surfaces
  Dynamic objects are removed
Free
Occupied
- a continuous set of LIDAR points, all static obstacles.
- Dynamic objects be removed: by removing all LIDAR points that are found within the bounding boxes of detected dynamic objects identified by the perception stack.
- all stationary objects such as poles, buildings, and parked cars, are shown as occupied grid cells.

## Slide 57: Detailed Roadmap
3 Methods of creation:
  Fully Online
    rarely used due to the complexity of creating such a map in real time
  Fully Offline
    unable to react or adapt to a changing environment
  Created Offline and Updated Online
- highly accurate
- 作り⽅：Specialized vehicles with high accuracy sensors are driven along roadways regularly to construct offline maps. Once the collection is complete, the information is then labelled with the use of a mixture of automatic labeling from static object perception and human annotation and correction.
- storing all the information present in a detailed roadmap called the lane length model
僕が開発しているMapAPIはDetailed Roadmap の一部になっている。静的な物体がないから
More about a highly detailed map used for autonomous driving:
[2014] Lanelets: Efficient map representation for autonomous driving
https://ieeexplore.ieee.org/abstract/document/6856487

## Slide 58: Detailed Roadmap
Traffic regulation Lane Boundaries

## Slide 59: Summary
Environmental maps used by self driving cars
Localization point cloud or feature map
Occupancy grid map
Detailed roadmap

## Slide 60: Module Summary
Understand various sensor and computing hardware used for autonomous driving
  The relative strengths and weaknesses
Understand the design of hardware sensor configurations for autonomous driving
Describe the basic architecture of a typical self-driving software system
  Understand the standard decomposition for each software module
Define the different types of maps used in autonomous driving