## Slide 1: コース 2 State Estimation and Localization for Self-Driving Cars
Localizationの定義：the method by which we determine the position and orientation of a vehicle within the world.
State Estimationの定義：the process of computing a physical quantity (that changes over time) like a position from a set of measurements.
Parameter Estimationの定義：a parameter is constant over time. 例えば、position and orientation are states of a moving vehicle, while the resistance of a particular resistor（抵抗器） in the electrical sub-system of a vehicle would be a parameter.

## Slide 2: Module 1 Least Squares

## Slide 3: Module 1 | Least Squares（最小二乗法）
In this module
The history of the method of least squares
Ordinary and weighted（加重） least squares
Recursive（再帰的） least squares（Kalman Filterに使われている）
Maximum likelihood and the method of least squares

## Slide 4: Module 1 | Lesson 1 (Part 1) The Squared Error（2乗誤差） Criterion and the Method of Least Squares

## Slide 5: Giuseppe Piazzi and Ceres
Giuseppe Piazzi
Piazzi’s 24 observations
Ceres
Ceres（ケレス）: the smallest dwarf planet（準惑星） in the solar system, located in the asteroid belt（小惑星帯）. It has a diameter of 930 kilometers.
準惑星：太陽の周囲を公転する惑星以外の天体のうち、それ⾃身の重⼒によって球形になれるだけの質量を有するもの。
Piazzi made 24 telescope（望遠鏡） observations of this new object over 40 days before it was lost in the glare（まぶしい光） of the sun.
- Since Ceres is only about 900km in diameter, finding it again was extremely challenging.
- This meant that other astronomers（天文学者、てんもん） could not confirm Piazzi’s discovery.
ジュゼッペ・ピアッツィ

## Slide 6: Karl Friedrich Gauss
Karl Friedrich Gauss ‘Princeps mathematicorum’
Gauss used the method of least squares to determine the orbital parameters of Ceres.
Carl Friedrich Gauss used a method of least squares to accurately estimate Ceres orbital（軌道） parameters based on Piazzi’s published measurements.

## Slide 7: Estimating Resistance
R?
Measurement | Resistance (Ohms)
1 | 1068
2 | 988
3 | 1002
4 | 996
the resistor has a gold band, which indicates that it can vary by as much as 5%.

## Slide 8: Estimating Resistance
y = x + v
Let x be the resistance. Assume it is a constant, but unknown.
We make measurements, y, of the resistance.
We model our measurements as corrupted by noise .
Measurement | Resistance (Ohms)
1 | 1068
2 | 988
3 | 1002
4 | 996

## Slide 9: Estimating Resistance
Measurement Model
‘Actual’ resistance Measurement noise
y1 = x + v1 y2 = x + v2 y3 = x + v3
y4 = x + v4
Measurement | Resistance (Ohms)
1 | 1068
2 | 988
3 | 1002
4 | 996

## Slide 10: Estimating Resistance
# | Resistance (Ohms)
1 | 1068
2 | 988
3 | 1002
4 | 996
y2 = x + v2
y3 = x + v3 y4 = x + v4
Measurement Model
y1 = x + v1
1
e2 = (y1 − x)2
Squared Error
2
e2 = (y2 − x)2
3
e2 = (y3 − x)2
4
e2 = (y4 − x)2
LS
x = argmin
x
(
2
e +
2
2
e + e + e
2
1 2 3 4
)
LS
= ℒ (x)
The squared error criterion:
The ‘best’ estimate of resistance is the one that minimizes the sum of squared errors

## Slide 11: Minimizing the Squared Error Criterion
e =
e1 e2 e3 e4
= y − Hx
=
y1 y2 y3 y4
−
1
1
1
1
x
Let’s re-write our criterion using vectors:
This matrix is called the ‘Jacobian’
LS
x = argmin
x
(
2
1
2
2
2
3
e + e + e + e
2
4
)
LS
= ℒ (x)

## Slide 12: Minimizing the Squared Error Criterion
1 2 3 4
ℒLS(x) = e2 + e2 + e2 + e2 = eTe
Now, we can express our criterion as follows,
= (y − Hx)T(y − Hx)
= yT y − xTHT y − yTHx + xTHTHx
LS
x = argmin
x
(
2
1
2
2
2
3
e + e + e + e
2
4
)
LS
= ℒ (x)
Transpose（転置）

## Slide 13: Minimizing the Squared Error Criterion
∂ℒ
∂x
x=x
= − yTH − yTH + 2xT̂ HTH = 0
−2yTH + 2xT̂ HTH = 0
To minimize this, we can compute the partial derivative（偏微分） with respect to our parameter, set to 0, and solve for an extremum:
Re-arranging, we arrive at:
xLS = (HTH)−1HT y
x-hat minimizes our squared error criterion!
ℒ(x) = eTe = yT y − xTHT y − yTHx + xTHTHx

## Slide 14: Minimizing the Squared Error Criterion
(HTH)−1 exists.
Careful! We will only be able to solve for x̂ if
This means that (HTH)−1 exists only if there are at least as many measurements as there are unknown parameters:
m ≥ n
HTH ∈ ℝn×n
H ∈ ℝm×n
If we have m
measurements, and n
unknown parameters, then:
HTH is not singular（特異行列）.
measurementsの数は最低parametersの数、これは当たり 前だ。
This will usually not be a problem. In fact, often face the challenge of dealing with too many measurements.
僕の理解、 (HTH)−1 が存在、つまりHTH!=0. HTHはm個方程式によって構成されて、未知数の数はn.
なので、m個方程式=0, n個未知数の場合、m<nなら必ず方程式の解が存在する。
逆行列

## Slide 15: Minimizing the Squared Error Criterion
Returning to our problem, we see that:
1
= [1111] 1
1
1
xLS = (HTH)−1HT y
−1
[1111]
1068
988
1002
996
4
= 1 (1068 + 988 + 1002 + 996) = 1013.5 Ohms
The least squares solution is just the mean of our measurements!
y =
1068
988
1002
996
H =
1
1
1
1
# | Resistance (Ohms)
1 | 1068
2 | 988
3 | 1002
4 | 996

## Slide 16: Method of Least Squares | Assumptions
Our measurement model, y = x + v, is linear.
Measurements are equally weighted.
(we do not suspect that some have more noise than others).
often broken in complex systems.

## Slide 17: Summary | The Method of Least Squares
Pioneered by Gauss to determine the orbit of the planetoid（小惑星） Ceres
Least squares finds the parameters which minimize the Least Squares Criterion（基準）
Ordinary least squares assumes that measurements are weighted equally, measurement model is linear

## Slide 18
Weighted Least Squares
Module 1 | Lesson 1 (Part 2)

## Slide 19: Method of Weighted Least Squares
Suppose we take measurements with multiple multimeters （回路計）, some of which are better than others
vs.

## Slide 20: Method of Weighted Least Squares
i
𝔼[v2] = σ2
(i = 1,…, m)
R = 𝔼[vvT] =
⋱
σ2
0
0
σ2
Consider the general linear measurement model for m measurements and n unknowns:
y1 x1 v1
⋮ = H ⋮ + ⋮
ym xn vm
y = Hx + v
In regular least squares, we implicitly assumed that each noise term was of equal variance（分散）:
One way to interpret the ordinary method of least squares is to say that we are implicitly assuming that each noise term is an independent random variable across measurements and has an equal variance or standard deviation. つまりI.I.D.条件。

## Slide 21: Method of Weighted Least Squares
𝔼[v2] = σ2, (i = 1,…, m)
i i
σ2
0
1
R = 𝔼[vvT] = ⋱
0
σ2
m
Then we can define a weighted least squares criterion as:
ℒWLS(x) = eTR−1e
1
σ2 σ2
2
e2 e2 e2
= 1 + 2 + … + m
σm2
e1 y1 x1
⋮ = e = ⋮ − H ⋮
em ym xn
where
If we assume each noise term is independent, but of different variance,
The higher the expected noise, the lower the weight we place on the measurement. （ノイズの分散が高ければ高いほど、ノイズに低い重みを置く）
Each squared error term is now weighted by the inverse of the variance associated with the corresponding measurement.
In other words, the lower the variance of the noise, the more strongly its associated error term will be weighted in the loss function.
We care more about errors which come from low noise measurements since those should tell us a lot about the true values of our unknown parameters.

## Slide 22: Re-deriving regular least squares
ℒWLS(x) = 1 + 2 + … + m
σ2 σ2 σ2
=
1
σ2
1
2 2
m
(e + … + e )
Since our variance is constant, it will not affect our final estimate! This results in the same estimate as regular least squares:
1 2
m
σ2 = σ2 = …σ2 = σ2 → x̂WLS = x̂LS = argmin x ℒLS(x) = argmin x ℒWLS(x)
What happens if all of our variances are the same?
e2 e2 e2

## Slide 23: Minimizing the Weighted Least Squares Criterion
x̂ = argmin x ℒ(x)
∂ℒ
∂x
x=x̂
= 0 = − yTR−1H + x̂THTR−1H
HTR−1Hx̂WLS = HTR−1y
The weighted normal equations!
Expanding our new criterion,
ℒWLS(x) = eTR−1e
= (y − Hx)TR−1(y − Hx)
We can minimize it as before, but accounting for the new weighting term:

## Slide 24: Method of Weighted Least Squares
Let’s adapt our example:
 | Resistance Measurements (Ohms) | 
# | Multimeter A ( σ = 20 Ohms ) | Multimeter B ( σ = 2 Ohms )
1 | 1068 | 
2 | 988 | 
3 |  | 1002
4 |  | 996
x̂ = (HTR−1H)−1HTR−1y
The weighted normal equations

## Slide 25: Method of Weighted Least Squares
xWLS = (HTR−1H)−1HTR−1y
= [1111]
400
400
4
4
−1
1
1
1
1
−1
[1111]
400
400
4
4
−1
1068
988
1002
996
=
1
1/400 + 1/400 + 1/4 + 1/4
(
1068 + 988 + 1002 + 996
400 400 4 4
)
= 999.3 Ohms
R =
σ2
1
2
σ2
σ2
3
2
σ4
=
400
400
4
4
y =
1068
988
1002
996
H =
1
1
1
1
Once we define the relevant quantities, we plug-and-chug to get:
It’s important to be comfortable working with different measurement variances（分散）and also with measurements that are sometimes correlated（相関）.
A self-driving car will have a number of different and complex sensors on board and we need to make sure that we model our error sources correctly.

## Slide 26: Ordinary versus Weighted Least Squares
Least Squares
Weighted Least Squares
Loss / Criterion
Solution
Limitations
ℒLS(x) = eTe
x̂LS = (HTH)−1HT y
m ≥ n
ℒWLS(x) = eTR−1e
x̂WLS = (HTR−1H)−1HTR−1y
m ≥ n
i
σ2 > 0
Accurate noise modelling is crucial to utilize various sensors effectively!

## Slide 27: Summary | Weighted Least Squares
Measurements can come from sensors that have different noisy characteristics
Weighted least squares lets us weight each measurement according to noise variance

## Slide 28
Module 1 | Lesson 2
Recursive（再帰的） Least Squares
1

## Slide 29: Batch Least Squares
xWLS = (HTR−1H)−1HTR−1y
‘Batch Solution’
 | Resistance Measurements (Ohms) | 
# | Multimeter A ( σ = 20 Ohms ) | Multimeter B ( σ = 2 Ohms )
1 | 1068 | 
2 | 988 | 
3 |  | 1002
4 |  | 996
In our previous formulation, we assumed we had all of our measurements available when we computed our estimate:

## Slide 30: Recursive Estimation
 | Resistance (Ohms) | 
Time | Multimeter A | Multimeter B
t = 1 sec | 1068 | 
t = 2 sec | 988 | 
t = 3 sec |  | 1002
t = 4 sec |  | 996
x1̂ = (HTR−1H)−1HTR−1y1
x2̂ = (HTR−1H)−1HTR−1y1:2
⋮
What happens if we have a stream（ストリーム） of data? Do we need to re-solve for our solution every time? Can we do something smarter?

## Slide 31: Linear Recursive Estimator
We can use a linear recursive estimator
Suppose we have an optimal estimate, x̂k−1, of our unknown parameters at time interval k -1
Then we obtain a new measurement at time k : yk = Hkx + vk
Goal: compute x̂k as a function of yk and x̂k−1 !
x̂k−1
x̂k
time
yk−1
yk
k - 1
k

## Slide 32: Linear Recursive Estimator
We can use a linear recursive update:
x̂k = x̂k−1 + Kk (yk − Hkx̂k−1)
We update our new state as a linear combination of the previous best guess and the current measurement residual（残余） (or error), weighted by a gain matrix （利得行列）Kk
x̂k−1
x̂k
yk−1
yk
k - 1
k
the term in brackets: innovation（測量値の差に近い意味）
- Innovation quantifies how well current measurement matches previous best estimate.

## Slide 33: Recursive Least Squares
But what is the gain matrix Kk ?
We can compute it by minimizing a similar least squares criterion, but this time we’ll use a probabilistic formulation.
We wish to minimize the expected value of the sum of squared errors of our current estimate at time step k :
ℒRLS = 𝔼[(xk − xk̂ )2]
If we have n
= σ2
k
unknown parameters at time step k ,we generalize this to
ℒRLS = 𝔼[(x1k − x1̂ k)2 + … + (xnk − xn̂ k)2]
= Trace(Pk)
Estimator covariance（共分散）
Trace（跡、せき）: In linear algebra, the trace (often abbreviated to tr) of a square matrix A is defined to be the sum of elements on the main diagonal （主対角線）(from the upper left to the lower right) of A.

## Slide 34: Recursive Least Squares
Using our linear recursive formulation, we can express covariance as a function of Kk
We can show (through matrix calculus) that this is minimized when
Kk = Pk−1HT(HkPk−1HT + Rk)−1
k k
With this expression, we can also simplify our expression for Pk :
Pk = Pk−1 − KkHkPk−1
= (1 − KkHk)Pk−1
Our covariance ‘shrinks’ with each measurement
Pk = (1 − KkHk)Pk−1(1 − KkHk)T + KkRkKT
k
証明なし
証明なし
The larger the gain matrix , the smaller the new estimator covariance will be. （利得行列が大きければ大きいほど、次周期の共分散が小さくなる）
Intuitively, think this gain matrix as balancing the information from prior estimate and the information from new measurement.

## Slide 35: Recursive Least Squares | Algorithm
1. Initialize the estimator
2. Set up the measurement model, defining the Jacobian and the measurement
covariance matrix:
3. Update the estimate of x̂k
yk = Hkx + vk
and the covariance Pk
using:
x̂0 = 𝔼[x]
P0 = 𝔼[(x − x̂0)(x − x̂0)T]
Kk = Pk−1HT(HkPk−1HT + Rk)−1
k k
x̂k = x̂k−1 + Kk (yk − Hkx̂k−1) Pk = (1 − KkHk)Pk−1
Important! Our parameter covariance ‘shrinks’ with each measurement
This initial guess could come from the first measurement and the covariance could come from technical specifications.
Recursive Least SquaresのImportance
Minimize computational effort in estimation process.
Forms the update step of the linear Kalman filter.
Linearモデル

## Slide 36: Summary | Recursive Least Squares
RLS produces a ‘running estimate’ of parameter(s) for a stream of measurements
RLS is a linear recursive estimator that minimizes the (co)variance of the parameter(s) at the current time
ランタイム予測

## Slide 37: Module 1 | Lesson 3 Least Squares and Maximum Likelihood

## Slide 38: Revisiting the Least Squares Criterion
•
Recall the least squares criterion
ℒLS(x) = (y1 − x)2 + (y2 − x)2 + … + (ym − x)2
We’ve said that the optimal estimate, x̂ , is the one that minimizes this ‘loss’:
x LS x
(
1
2
xLS = argmin ℒ (x) = argmin e + e + … + e
2 2 2
m
)
Why squared errors?
計算簡単：If the measurement model is linear, minimizing the squared error criterion amounts to solving a linear system of equations.
Probability and a deep connection between least squares and maximum likelihood estimators under the assumption of Gaussian noise.

## Slide 39: Least Squares and Maximum Likelihood
Karl Friedrich Gauss ‘Princeps mathematicorum’
Gauss showed the connection between his method of least squares and maximum likelihood with Gaussian measurement models

## Slide 40: The Method of Maximum Likelihood（尤度）
p(y | xb)
p(y | xa)
p(y | xc)
p(y | xd)
y
ymeas
Which x is the most likely given the measurement?
x̂ = argmax x p(y | x)
We can ask which x makes our measurement (y) most likely. Or, in other words,
which x
maximizes the conditional probability of y :

## Slide 41: Measurement Model
p(y | x)
y = x
p(y | x) = 𝒩(x, σ2)
Recall our simple measurement model:
y = x + v
We can convert this into a conditional probability on our measurement, by assuming some probability density for v . For example, if
v ∼ 𝒩(0, σ2)
Then:
The unknown parameter x becomes the mean of this density, and the variance is noise variance.

## Slide 42: Least Squares and Maximum Likelihood
=
1
2πσ2
e
−(y − x)2
2σ2
=
1 (2π)mσ2m
exp
(
−∑m (yi − x)2
i=1
2σ2
)
If we have multiple independent measurements, then:
p(y | x) ∝ 𝒩(y1; x, σ2)𝒩(y2; x, σ2) × … × 𝒩(ym; x, σ2)
2
1
σ 2π
Our conditional measurement likelihood is
p(y | x) = 𝒩(y; x, σ2)
𝒩(z; μ, σ ) = e
−(z − μ)2
2σ2
Probability density function（確率密度関数） of a Gaussian is:

## Slide 43: Least Squares and Maximum Likelihood
xMLE = argmax x p(y | x)
= argmax x log p(y | x)
Resulting in:
2σ2
log p(y | x) = − 1 ((y − x)2 + … + (y − x) 2 ) + C
1 m
The maximal likelihood estimate (MLE, 最尤推定) is given by
xMLE = argmax x p(y | x)
Instead of trying to optimize the likelihood directly, we can take its logarithm:
The logarithm is monotonically increasing!（単調増加）
足し算

## Slide 44: Least Squares and Maximum Likelihood
Since
argmax z f(z) = argmin z (−f(z))
2σ2
1
= argmin x ((y1 − x)2 + … + (ym − x)2)
The maximal likelihood problem can therefore be written as
xMLE = argmin x − (log p(y | x))

## Slide 45: Least Squares and Maximum Likelihood
So:
MLE
x = argmin
x
1
2σ
2
(
1
2
(y − x) + … + (y
m
− x)
2
)
In both cases, 最尤推定の答えと最小二乗の答えが一緒！
xMLE = xLS = argmin x ℒLS(x) = argmin x ℒMLE(x)
MLE
x̂ = argmin
x
(y1 − x)2 + … + (ym − x)2
Finally, if we assume each measurement has a different variance, we can derive

## Slide 46: The Central Limit Theorem（中心極限定理）
In realistic systems like self driving cars, there are many sources of ‘noise’
Why use the method of least squares?
  Central Limit Theorem: sum of different errors will tend be ‘Gaussian’-ish
  Least squares is equivalent to maximum likelihood under Gaussian noise
Central Limit Theorem: When independent random variables are added, their normalized sum tends towards a normal distribution. 独立の確率変数の正規された和が正規分布になりそう。
model system probabilistically and yet maintain simplicity in calculations.

## Slide 47: Least Squares | Some Caveats（警告）
‘Poor’ measurements (e.g. outliers, 外れ値) have a significant effect on the method of least squares
It’s important to check that the measurements roughly follow a Gaussian distribution
# | Resistance (Ohms)
1 | 1068
2 | 988
3 | 1002
4 | 996
x̂ = 1013.
# | Resistance (Ohms)
1 | 1068
2 | 988
3 | 1002
4 | 996
5 (outlier) | 1430
x̂ = 1096.8
Under the Gaussian PDF, samples ‘far away’ from the mean are ‘very improbable’

## Slide 48: Summary | Least Squares and Maximum Likelihood
LS and WLS produce the same estimates as maximum likelihood assuming Gaussian noise
Central Limit Theorem states that complex errors will tend towards a Gaussian distribution.
Least squares estimates are significantly affected by outliers