## Slide 1: MODULE 2 LINEAR AND NONLINEAR KALMAN FILTERS

## Slide 2: Module 2 | Linear and Nonlinear Kalman Filters
In this module…
A brief history and overview of the (linear) Kalman filter
Kalman filter as the BLUE
Extending the Kalman filter to nonlinear systems through linearization
Limitations of linearization
Unscented Kalman filter
In today’s world of advanced machine learning, the Kalman filter remains an important tool to fuse measurements from several sensors to estimate in real-time the state of a robot system such as a self-driving car.
a modern alternative to linearization through the unscented transform.
(best Linear Unbiased Estimator)

## Slide 3: MODULE 2 LESSON 1 THE KALMAN FILTER

## Slide 4: The Kalman Filter
Rudolf E. Kálmán receiving the National Medal of Science

## Slide 5: The Kalman Filter
Apollo Guidance Computer
The (extended) Kalman Filter became widely known after its use in the Apollo Guidance Computer（アポロ誘導コンピューター） for circumlunar（月の周りをまわる） navigation.

## Slide 6: The Kalman Filter | Prediction and Correction
𝒩(xk̂ −1, P̂k−1)
PDF
Estimate at (k - 1)
Position(p)
Prediction
(Motion Model)
𝒩(xˇk, Pˇk)
1. Prediction
Measurement
(Observation Model)
𝒩(yk, Rk)
e.g.,
wheel odometry, inertial navigation
e.g., GPS,
Lidar
𝒩(xk̂ , P̂k)
3. Fusion
2. Measurement
Estimate at (k)
The Kalman filter is very similar to the linear recursive least squares filter. 僕はMPCを思いついた。
While recursive least squares updates the estimate of a static parameter, Kalman filter is able to update the estimate of an evolving state.
1D Example（⼤事）
Starting from an initial probabilistic estimate at time k-1, the goal is to use a motion model which could be derived from wheel odometry or inertial sensor measurements to predict our new state.
Use the observation model derived from GPS for example, to correct that prediction of vehicle position at time k.
Each of these components, the initial estimate, the predicted state, and the final corrected state are all random variables that will be specified by their means and covariances. （各状態は確率変数として、平均値や共分散で表す）
  In this way, Kalman filter can be seen as a technique to fuse information from different sensors to produce a final estimate of some unknown state, taking into account uncertainty in motion and in measurements.

## Slide 7: The Kalman Filter | Linear Dynamical System
The Kalman Filter requires the following motion and measurement models:
With the following noise properties:
vk ∼ 𝒩(0, Rk)
Measurement Noise
wk ∼ 𝒩(0, Qk)
Process or Motion Noise
xk = Fk−1xk−1 + Gk−1uk−1 + wk−1
Motion model:
input
noise
Measurement model:
yk = Hkxk + vk
noise
control input
zero-mean noise
u: an external signal that affects the evolution of system state. In the context of self-driving vehicles, this may be a wheel torque（車輪トルク） applied to speed up and change lanes, for example. Actuator signal (throttle / brake / steering)でしょう。

## Slide 8: The Kalman Filter | Recursive Least Squares + Process Model
The Kalman filter is a recursive least squares estimator that also includes a motion model
xˇ
Prediction
k (given motion model)
at time k
x̂k
Corrected prediction (given measurement) at time k
Pˇ = F P
k k−1 k−1
̂ FT
k−1
+ Q
k−1
Prediction
xˇk = Fk−1xk−1 + Gk−1uk−1
1
Kk = PˇkHT(HkPˇkHT + Rk)−1
k k
2a Optimal Gain
x̂k = xˇk + Kk(yk − Hkxˇk)
P̂k = (1 − KkHk)Pˇk
Correction
2b
(yk − Hkxˇk)
is often called the ‘innovation’
1 Prediction: Use the process model (motion model) to predict how states (evolving states and non-state parameters) evolved since the last time step. Propagate mean and uncertainty (covariance).
因みにrecursive least squaresのoptimal gainの計算式は：
Kalman Filterは前周期の共分散ではなく、現在周期の Motion Modelのノイズを考慮したあとの共分散を使っている。
2b Correction: use optimal gain to propagate the state covariance from prediction to corrected state.

## Slide 9
The Kalman Filter | Prediction & Correction
𝒩(xk̂ −1, P̂k−1)
PDF
Position(x)
𝒩(xˇk, Pˇk)
𝒩(yk, Rk)
𝒩(xk̂ , P̂k)
1. Prediction
3. Correction
2. Measurement
xˇk = Fk−1xk−1 + Gk−1uk−1
ˇ
P
k
̂
= F P
k−1 k−1
F
T
k−1
+ Qk−1
1. Prediction
{
2,3. Measurement & Correction
k k k k k k
P̂k = (1 − KkHk)Pˇk
{ x̂ = xˇ + K (y − H xˇ )
k k
Kk = PˇkHT(HkPˇkHT + Rk)−1
Kはまず測量モデルのノイズを伝播している。また、測量値（厳密にいうと、Innovation）が新状態での割合も決めている。

## Slide 10: The Kalman Filter | Short Example
PDF
Position(p)
x =
[
dp
dt
·
p
= p
]
2
u = a = d p
dt2
k
x =
[
1 Δt
0 1
xk−1 +
] [
0
Δt
]
k−1
u + w
k−1
Motion/Process Model
wk ∼ 𝒩(0, (0.1)12×2)
yk = [1 0] xk + vk
Noise Densities
vk ∼ 𝒩(0, 0.05)
Position Observation
H
F
G
R
Q
pだけを観察している

## Slide 11: The Kalman Filter | Short Example
PDF
Position(p)
Data
̂
0
x ∼ 𝒩(
5
[ ]
,
[
0 0.01 0
0 1
]
)
Δt = 0.5s
u0 = − 2 [m/s2]
y1 = 2.2 [m]

## Slide 12: The Kalman Filter | Short Example Solution
Prediction
xˇk = Fk−1xk−1 + Gk−1uk−1
[
pˇ1
ˇ
·
p
1
]
= 1 0.5 0 +
[ ] [ ] [
0 (−2) = 2.5
0 1 5 0.5 4
] [ ]
k−1
Pˇk = Fk−1P̂k−1FT + Qk−1
ˇ
P
1
=
0 1
[ ] [
] [
1 0.5 0.01 0 1 0.5
0 1 0 1
T
+
] [
0.1 0
0 0.1
=
] [
0.36 0.5
0.5 1.1
]

## Slide 13: The Kalman Filter | Short Example Solution
Correction
K1 = Pˇ1HT(H1Pˇ1HT + R1)−1
1 1
=
[
0.36 0.5 1
0.5 1.1 0
] [ ]
(
1 0
[ ]
[
0.36 0.5
1
0.5 1.1 0
] [ ]
+ 0.05
)
−1
=
[
0.88
1.22
]
p̂1
̂
·
p
1
]
4
[ ] [
1.22 4
= 2.5 + 0.88 (2.2 − [1 0] 2.5 ) = 2.24
3.63
] [ ] [ ]
x̂1 = xˇ1 + K1(y1 − H1xˇ1)
Bonus!
P̂1 = (1 − K1H1)Pˇ1
=
[
0.04 0.06
0.06 0.49
[
]
corrected state variance is smaller. This uncertainty reduction occurs because measurement model is fairly accurate. つまりvk
のvariance (0.05)が小さい。
位置の予測値は2.5m, 測量値が2.2m, Kalman Filterは2.24mに修正した。

## Slide 14: Summary | The Kalman Filter
The Kalman Filter is very similar to RLS but includes a motion model that tells us how the state evolves over time. RLSの方はstateが変わらない。
The Kalman Filter updates a state estimate through two stages:
  prediction using the motion model
  Correction（訂正、修正） using the measurement model

## Slide 15: MODULE 2 LESSON 2 THE KALMAN FILTER: BIAS BLUES

## Slide 16: Bias in State Estimation
Drive the car for K time steps, record estimation error, repeat…..
We say an estimator or filter is unbiased if it produces an ‘average’ error of zero at a particular time step k, over many trials（同じタイミングのトライアル）
Process/Motion:
Measurement:
xk = Fk−1xk−1 + Gk−1uk−1 + wk−1 yk = Hkxk + vk
k = 0, 1, …. K

## Slide 17: Bias in State Estimation
PDF
Position (at time k)
pk
True
Position
{p̂k}
E[p̂k]
Mean of Estimated Position Values
Bias
E[p̂k] − pk
This filter is an unbiased if for all k,
E[ek̂ ] = E[p̂k − pk] = E[p̂k] − pk = 0
Build a histogram of the positions that the filter reports over multiple trials.
Compute the difference between the average of these estimates and the true position.
If this difference does approach zero as repeating this experiment many more times, and if this happens for all time intervals, then the filter is unbiased.

## Slide 18: Bias in State Estimation
How can we compute this analytically for the Kalman filter?
Consider the error dynamics:
ek̂ = x̂k − xk
Corrected estimate error
eˇk = xˇk − xk
Predicted state error
Using the Kalman Filter equations, we can derive:
eˇk = Fk−1eˇk−1 − wk
ek̂ = (1 − KkHk)eˇk + Kkvk
証明なし…

## Slide 19: Bias in State Estimation
For the Kalman filter, for all k,
E[eˇk] = E[Fk−1eˇk−1 − wk]
= Fk−1E[eˇk−1] − E[wk]
Note: this does not mean that the error on a given trial will be zero, but that, with enough trials, our expected error is zero!
Unbiased predictions!
E[ek̂ ] = E[(1 − KkHk)eˇk + Kkvk]
= (1 − KkHk)E[eˇk] + KkE[vk]
= 0
= 0
E[v] = 0 E[w] = 0
+ white, uncorrelated noise
So long as E[e0̂ ] = 0
この条件だった ら、証明は簡単。

## Slide 20: Consistency in State Estimation
PDF
{p̂k}
2
E[ek̂ ]
k
k =
E[e2̂ ] ? P
k
E[e2̂ ] = E[(p̂k − pk)2] = P̂k
Position (at time k)
This filter is consistent if for all k,
Practically, this means that our filter is neither overconfident, nor under confident in the estimate it has produced.
overconfident filter: essentially place too much emphasis on its own estimate and be less sensitive to future measurement updates.
easy to see how an overconfident filter might have a negative or dangerous effect on the performance of self-driving car.
予測器でサンプリングしたサンプルの分散の期待値が、予測されたパラメータ自体の分散と同じ。

## Slide 21: Consistency in State Estimation
0
E[e0̂ eT̂ ] = Pˇ 0
E[v] = 0 E[w] = 0
+ white noise
One can also show (with more algebra!) that for all k,
E[eˇkeˇT] = Pˇ k E[ek̂ eT̂ ] = P̂k
k k
Consistent predictions!
Provided,
証明なし…
Pはxの共分散

## Slide 22: The Kalman Filter is the BLUE Best Linear Unbiased Estimator
We’ve shown that given our linear formulation, and zero-mean, white noise the Kalman Filter is unbiased
We can also say that the filter is consistent:
E[ek̂ ] = 0
In general, if we have white, uncorrelated zero-mean noise, the Kalman filter is the best (i.e., lowest variance（これも証明なしだろう…）) unbiased estimator that uses only a linear combination of measurements
For this reason, we call it the BLUE (best linear unbiased estimator)
k
E[ek̂ eT̂ ] = P̂k
However, most real systems are not linear.
For self-driving cars, generally need to estimate non-linear quantities like vehicle poses, position, and orientation in 2D and 3D.
例えば、AWGN,加算性白色ガウス雑音

## Slide 23: Summary | The Kalman Filter and The Bias BLUEs
The Kalman filter is
unbiased
consistent
the lowest variance estimator that uses a linear combination of measurements: Best Linear Unbiased Estimator (BLUE)

## Slide 24
GOING NONLINEAR: THE EXTENDED KALMAN FILTER
MODULE 2 LESSON 3

## Slide 25
1. Prediction
PDF
Position(x)
𝒩(xˇk, Pˇk)
𝒩(yk, Rk)
{Pˇ = F P
k k−1 k−1
̂ FT
k−1
+ Q
k−1
xˇ = F x + G u
k k−1 k−1 k−1 k−1
𝒩(xk̂ −1, P̂k−1)
1. Prediction
2/3. Measurement & Correction
k k
x̂ = xˇk + Kk(y − Hkxˇk)
P̂k = (1 − KkHk)Pˇk
{
k k
Kk = PˇkHT(HkPˇkHT + Rk)−1
Linear discrete-time Kalman Filter:
𝒩(xk̂ , P̂k)
Linear motion / process model
xk = Fk−1xk−1 + Gk−1uk−1 + wk−1
previous inputs state
process noise
current state
wk ∼ 𝒩(0, Qk)
measurement
measurement noise
state
Linear measurement model
yk = Hkxk + vk
vk ∼ 𝒩(0, Rk)
3. Correction
2. Measurement
Recap | The Linear Kalman Filter

## Slide 26: Nonlinear Kalman Filtering
Linear systems do not exist in reality!
I = V/R
Ohm’s Law（オームの法則）:
Current
Linear regime
Nonlinear regime
Voltage
xk = fk−1(xk−1, uk−1, wk−1)
yk = hk(xk, vk)
How can we adapt the Kalman Filter to nonlinear discrete-time systems?
previous inputs state
process noise
current state
measurement
measurement noise
state

## Slide 27: EKF | Linearizing a Nonlinear System f(x)
Mathematically, we compute this linear approximation using a first-order Taylor expansion:
First-order（一次） terms
Higher-order terms
Choose an operating point a and approximate the nonlinear function by a tangent line at that point
a
x
f(a)
slope = ∂f(x)
∂x
x=a

## Slide 28: EKF | Linearizing a Nonlinear System
xk = fk−1(xk−1, uk−1, wk−1) ≈ fk−1(x̂k−1, uk−1, 0) + ∂fk−1
∂xk−1
x̂k−1,uk−1,0
Fk−1
(xk−1 − x̂k−1) + ∂fk−1
∂wk−1
x̂k−1,uk−1,0
Lk−1
wk−1
For the EKF, we choose the operating point to be our most recent state estimate, our known input, and zero noise:
Linearized motion model
yk = hk(xk, vk) ≈ hk(xˇk, 0) + ∂hk
∂xk
xˇk,0
∂vk
xˇk,0
Hk Mk
We now have a linear system in state-space! The matrices Fk–1, Lk–1, Hk, and Mk are called the Jacobian matrices of the system
(xk − xˇk) + ∂hk vk
Linearized measurement model
wは0で展開しているので、w-0=w
uは既知（きち）なので、u-u=0

## Slide 29: EKF | Computing Jacobian Matrices
In vector calculus, a Jacobian matrix is the matrix of all first-order partial derivatives of a vector-valued function
∂f
∂x =
[ ∂f
∂x1
⋯
∂f
n
∂x ]
=
∂f1
∂x1
∂f1
∂xn
⋯
⋮ ⋱ ⋮
∂fm ⋯ ∂fm
∂x1 ∂xn
Intuitively, the Jacobian matrix tells you how fast each output of the function is changing along each input dimension
For example:
f(x) =
f
1
f
2
=
[ ] [
x + x
1 2
2
x1
∂x
∂f =
∂f1 ∂f1
∂x1 ∂x2
∂f2 ∂f2
∂x1 ∂x2
=
[
1 1
1
2x 0
]
]

## Slide 30: EKF | Putting It All Together
With our linearized models and Jacobians, we can now use the Kalman Filter equations!
Kk = PˇkHT(HkPˇkHT + MkRkMT)−1
k k k
xˇk
Correction
x̂k = xˇk + Kk(yk − hk(xˇk, 0))
P̂k = (1 − KkHk)Pˇk
Prediction (given motion model)
at time k
Pˇk = Fk−1P̂k−1FT 1 + Lk−1Qk−1LT 1
k− k−
x
̂ Corrected prediction
k (given measurement)
at time k
Linearized motion model
xk = fk−1(x̂k−1, uk−1, 0) + Fk−1 (xk−1 − x̂k−1) + Lk−1wk−1
Prediction
xˇk = fk−1(x̂k−1, uk−1, 0)
Linearized measurement model
yk = hk(xˇk, 0) + Hk (xk − xˇk) + Mkvk
Optimal gain
Linear Kalman Filterの式との区別
First, in the prediction and correction steps, still use the nonlinear models to propagate the mean of the state estimate and to compute the measurement residual or innovation.
  理由：linearize motion model about the previous state estimate, linearize the measurement model about the predicted state.
  By definition, the linearized model exactly coincides with the nonlinear model at the operating point.
Second, the appearance of L and M Jacobians related to the process and measurement noise.
  In many cases, both of these matrices will be identity（単位行列） since noise is often assumed to be additive（加算）. （つまり非線形システムの中にもノイズは+w / +vの形で、w, vに対するヤコビ行列は単位行列になる）
Nonlinear伝播の部分

## Slide 31: EKF | Short Example
Position
Height
x =
p
·
p
[ ]
··
u = p
ϕ
p
D
S
S
k
( D − p )
= tan−1 + vk
wk ∼ 𝒩(0, (0.1)12×2)
Motion/Process model
xk = f(xk−1, uk−1, wk−1)
Noise densities
vk ∼ 𝒩(0, 0.01)
Landmark measurement model
yk = ϕk = h(pk, vk)
S and D are known in advance
=
[ ]
k−1
x +
1 Δt 0
0 1 Δt
[ ]
k−1
u + w
k−1
Motion modelはまだlinear, Measurement modelはnonlinear.
加算ノイズ、なのでvに対するヤコビ行列は単位行列になる。

## Slide 32: EKF | Short Example
Measurement model Jacobians
k
H = ∂h
∂xk
xˇk,0
=
S
k
(D − pˇ )
2
2
0
+ S
+
∂h
Mk =
∂vk
xˇk,0
= 1
Motion model Jacobians
∂f
Fk−1 =
∂xk−1
x̂k−1,uk−1,0
=
[
1 Δt
0 1
]
k−1
L =
∂f
∂wk−1
x̂k−1,uk−1,0
= 1
2×2
Position
Height
ϕ
p
D
S
[
]

## Slide 33: EKF | Short Example
Data
x̂0 ∼ 𝒩
(
5
[ ]
,
[
0 0.01 0
0 1
]
)
Δt = 0.5 s
Using the Extended Kalman Filter equations, what is our updated position?
p̂1
u0 = − 2 [m/s2]
S = 20 [m]
y1 = π/6 [rad]
D = 40 [m]
Position
Height
ϕ
p
D
S

## Slide 34: EKF | Short Example Solution
xˇ1 = f0(x̂0, u0, 0)
pˇ1
ˇ·
1
p
=
[
1 0.5
0
+
0
0 1 5 0.5
] [ ] [ ]
(−2) =
[
2.5
4
]
ˇ
P
1
=
[ ] [
] [
+
] [ ] [
1 0.5 0.01 0 1 0 1 0 0.1 0 1 0
0 1 0 1 0.5 1 0 1 0 0.1 0 1
=
] [ ] [
0.36 0.5
0.5 1.1
]
Prediction
Pˇ1 = F0P̂0FT + L0Q0LT
0 0
This is the same result as in the linear Kalman Filter example because the motion model is already linear!
]
[

## Slide 35: EKF | Short Example Solution
p̂1
̂
·
1
p
4
[ ] [
0.55
= 2.5 + 0.40 (0.52 − 0.49) = 2.51
4.02
] [ ]
P̂1 = (1 − K1H1)Pˇ1
Correction
K1 = Pˇ1HT(H1Pˇ1HT + M1R1MT)−1
1 1 1
Bonus!
=
[ ] [
0.36 0.5 0.011
0.5 1.1 0
]
(
[
0.011 0
]
[
0.5 1.1
] [
0.36 0.5 0.011
0
]
+ 1(0.01)(1)
)
−1
=
[
0.40
0.55
]
=
[
0.36 0.50
0.50 1.1
]
x̂1 = xˇ1 + K1(y1 − h1(xˇ1, 0))
[
]
In this case, even though the corrected mean of the state estimate ([2.51 4.02) is different from the predicted mean ([2.5 4), the corrected covariance didn’t change that much from the predicted covariance.
理由：This is because the azimuth angle changes slowly at this distance, and doesn’t provide much information about the vehicle state compared to a GPS measurement.

## Slide 36: Summary | Extended Kalman Filter (EKF)
The EKF uses linearization to adapt the Kalman filter to nonlinear systems
Linearization works by computing a local linear approximation（近似） to a nonlinear function about a chosen operating point
Linearization relies on computing Jacobian matrices, which contain all the first- order partial derivatives of a function

## Slide 37: MODULE 2 LESSON 4 AN IMPROVED EKF: THE ERROR- STATE EXTENDED KALMAN

## Slide 38: What’s in a State?
We can think of the vehicle state as composed of two parts:
x = x̂ + δx
True State
Nominal State (“Large”)
Error State (“Small”)
We can continuously update the nominal state by integrating the motion model
accumulate into the error state
Time
Position
True state
̂ • Modelling errors and process noise
Nominal state x
Error state δ

## Slide 39: The Error-State Extended Kalman Filter
The Error-State Extended Kalman Filter estimates the error state directly and uses it as a correction to the nominal state:
Linearized motion model
xk = fk−1(x̂k−1, uk−1, 0) + Fk−1 (xk−1 − x̂k−1) + Lk−1wk−1
Linearized measurement model
yk = hk(xˇk, 0) + Hk (xk − xˇk) + Mkvk
δxk
δxk−1
xk − fk−1(x̂k−1, uk−1, 0) = Fk−1 (xk−1 − x̂k−1) + Lk−1wk−1
yk = hk(xˇk, 0) + Hk (xk − xˇk) + Mkvk
δxk
Error state
Error state
Motion modelの式からError stateは線形モデルで伝播していると思う。Measurement modelの式はEKFと同じくLocal Linearizationで計算している。

## Slide 40: The Error-State Extended Kalman Filter
Loop:
1. Update nominal state with motion model
xˇk = fk−1(xk−1, uk−1, 0)
This could be
xˇk−1 or x̂k−1
measurementはまだ（センサーから）来ていないかもしれないから。

## Slide 41: The Error-State Extended Kalman Filter
Loop:
Update nominal state with motion model
Propagate uncertainty
Pˇ k = Fk−1Pk−1FT 1 + Lk−1Qk−1LT 1
k− k−
This could be
Pˇ k−1 or P̂k−1
depending on whether we used a measurement to do a correction step
Motion modelでのerror stateの伝播は共分散Pの中に行われていると思う。

## Slide 42: The Error-State Extended Kalman Filter
Loop:
Update nominal state with motion model
Propagate uncertainty
If a measurement is available:
  Compute Kalman Gain
Kk = Pˇ kHT(HkPˇ kHT + R)−1
k k
Repeat 1, 2 until a measurement is available and we want to do a correction
Mがない、 多分Identityだから、EKFと⼀緒

## Slide 43: The Error-State Extended Kalman Filter
Loop:
Update nominal state with motion model
Propagate uncertainty
If a measurement is available:
  Compute Kalman Gain
  Compute error state
δx̂k = Kk(yk − hk(xˇk, 0))

## Slide 44: The Error-State Extended Kalman Filter
Loop:
Update nominal state with motion model
Propagate uncertainty
If a measurement is available:
  Compute Kalman Gain
  Compute error state
  Correct nominal state
x̂k = xˇk + δx̂k

## Slide 45: The Error-State Extended Kalman Filter
Loop:
Update nominal state with motion model
Propagate uncertainty
If a measurement is available:
  Compute Kalman Gain
  Compute error state
  Correct nominal state
  Correct state covariance
P̂k = (1 − KkHk)Pˇ k
（EKFと⼀緒）

## Slide 46: Why Use the ES-EKF?
1. Better performance compared to the vanilla EKF
The “small” error state is more amenable（従順、じゅうじゅん） to linear filtering than the “large” nominal state, which can be integrated nonlinearly
2. Easy to work with constrained quantities (e.g., rotations in 3D)
We can also break down the state using a generalized composition operator
x = x̂ ⊕ δx
True State
Nominal State (Overparametrized, constrained)
Error State (Minimal parametrization,
unconstrained)
この点について更に説明はできていないですが、以前2輪ロボットの運動はtanθ=dy/dxで拘束されることを紹介していました。
（generalized composition（合成） operatorで具体的にどこ変わったかまだ分かっていない）
Motion modelの適用周期やMeasurement modelの適用周期が一緒だったら、EKFと一緒だと思う。
自分の考え：小さい値の方を線形でモデリングしやいと言っていると思う。例えばθが小さい時、非線形のsinθ, tanθなどをθでモデリングしても問題なさそうです。

## Slide 47: Summary | The Error-State EKF (ES-EKF)
The error-state formulation separates the state into a “large” nominal state and a “small” error state.
The ES-EKF uses local linearization to estimate the error state and uses it to correct the nominal state.
The ES-EKF can perform better than the vanilla EKF, and provides a natural way to handle constrained quantities like rotations in 3D.
the evolution of the error state tends to be closer to linear.

## Slide 48
MODULE 2 LESSON 5
LIMITATIONS OF THE EXTENDED KALMAN FILTER
1

## Slide 49: Limitations of the EKF | Linearization error
The EKF works by linearizing the nonlinear motion and measurement models to update the mean and covariance of the state
a
x
f(a)
slope = ∂f(x)
∂x
x=a
f(x) ≈ f(a) + ∂f(x)
∂x
(x − a)
x=a
In general, linearization error depends on
How nonlinear the function is
How far away from the operating point the linear approximation is being used（operating pointでの値と同じ、離れたら線形化エラーが大きくなる）
The difference between the linear approximation and the nonlinear function is called linearization error
Linearization error
f(x)

## Slide 50: Linearization Error | Example
1.01
1.00
0.99
0.98
y0.97
0.96
0.95
0.94
0.93
—0.4 —0.2 0.0 0.2 0.4
x
1.01
1.00
0.99
0.98
y0.97
0.96
0.95
0.94
0.93
—0.4 —0.2 0.0 0.2 0.4
x
1.01
1.00
0.99
0.98
y0.97
0.96
0.95
0.94
0.93
—0.4 —0.2 0.0 0.2 0.4
x
1.01
1.00
0.99
0.98
y0.97
0.96
0.95
0.94
0.93
—0.4 —0.2 0.0 0.2 0.4
x
1.01
1.00
0.99
0.98
y0.97
0.96
0.95
0.94
0.93
—0.4 —0.2 0.0 0.2 0.4
x
1.01
1.00
0.99
0.98
y0.97
0.96
0.95
0.94
0.93
—0.4 —0.2 0.0 0.2 0.4
x
—0.4
—0.2
0.2
0.4
0.0
x
0.93
0.94
0.95
0.96
0.97
0.98
0.99
1.00
1.01
y
1.9
1.8
1.7
1.6
✓
1.5
1.4
1.3
1.2
0.985 0.990 0.995 1.000 1.005 1.010 1.015
r
1.9
1.8
1.7
1.6
✓
1.5
1.4
1.3
1.2
0.985 0.990 0.995 1.000 1.005 1.010 1.015
r
1.2
1.3
1.4
1.5
1.6
1.7
1.8
1.9
✓
Polar coordinates（極座標系）
True mean
Linearized mean
True mean
True covariance
0.985 0.990 0.995 1.000 1.005 1.010 1.015
r True covariance
Linearized
covariance Cartesian coordinates（直交座標系）
x = r cos θ y = r sin θ
Nonlinear transformation
Let’s look at an example of how linearization error affects the mean and covariance of a random variable transformed by a nonlinear function:
Linearized transformation
x ≈ r¯ cos θ¯ + cos θ¯ (r − r¯)
−r¯ sin θ¯ (θ − θ¯)
y ≈ r¯ sin θ¯ + sin θ¯ (r − r¯)
+r¯ cos θ¯ (θ − θ¯)
この例のpolar coordinatesからcartesian coordinatesへの変換はLidarに関するmeasurementによく ある。
結果：The mean of the linearized distribution is in a very different place from the true mean, and the linearized covariance seriously underestimates （過小評価） the spread of the true output distribution along the y dimension.
問題シーン：For example, the estimated position of lane markers produced from a laser scanner might differ significantly from the actual positions, leading our car to drive over the center line.

## Slide 51: Limitations of the EKF | Linearization Error
The EKF is prone to linearization error when
The system dynamics are highly nonlinear
The sensor sampling time is slow relative how fast the system is evolving（つまりMotionモデルがhigh rate, Measurementがlow rate）
This has two important consequences:
The estimated mean state can become very different from the true state
The estimated state covariance can fail to capture the true uncertainty in the state
Linearization error can cause the estimator to be overconfident in a wrong answer!
For self-driving cars moving very fast relative to the sampling time of your sensors, you’re going to get more linearization error than if it’s moving slowly.
If your car’s estimator diverges while driving, it could easily drive off the road into a ditch（溝） or cause a collision with another vehicle.

## Slide 52: Limitations of the EKF | Computing Jacobians
Computing Jacobian matrices for complicated nonlinear functions is also a common source of error in EKF implementations!
Analytical differentiation is prone to human error
Numerical differentiation（数値微分） can be slow and unstable
Automatic differentiation (e.g., at compile time) can also behave unpredictably
What if one or more of our models is non-differentiable?
Do we really need linearization for nonlinear Kalman filtering?
例えば

## Slide 53: Summary | Limitations of the EKF
The EKF uses analytical local linearization and, as a result, is sensitive to linearization errors
For highly nonlinear systems, the EKF estimate can diverge（逸れる、それる） and become unreliable
Computing complex Jacobian matrices is an error-prone process and must be done with substantial care
6

## Slide 54
MODULE 2 LESSON 6
AN ALTERNATIVE TO THE EKF: THE UNSCENTED KALMAN FILTER
1
Unscented: 無臭（むしゅう）、無香料（こうりょう）
Unscented Transform gives much higher accuracy than analytical EKF style linearization, for a similar amount of computation, and without needing to compute any Jacobians.

## Slide 55: The Unscented Transform
“It is easier to approximate a probability distribution than it is to approximate an arbitrary nonlinear function” — S. Julier, J. Uhlmann, and H. Durrant-Whyte (2000)
p(x)
1. Choose sigma points
3. Compute weighted mean and covariance of transformed sigma
points
μx
σx σx
p(y)
y
σ σy
y
μy
y = h(x)
2. Transform sigma points
These aren’t random samples, they’re deterministic samples chosen to be a certain number of standard deviations away from the mean.
The Unscented Transform is sometimes called the Sigma Point Transform.

## Slide 56: The Unscented Transform | Choosing Sigma Points
x = μ
0 x
xi = μx +
xi+N = μx −
i = 1, …, N i = 1, …, N
N + κ coliL
N + κ coliL
For an N-dimensional PDF 𝒩(μx, Σxx) , we need 2N + 1 sigma points:
LLT = Σxx
(L lower triangular)
κ = 3 − N
for Gaussian PDFs
p(x)
μx
σx σx
μx + 3σx
μx − 3σx
x0
x
1
x
2
𝒩(μx, Σxx)
x
0
x1
x2
x3
x4
μ
x
1. Compute the Cholesky Decomposition of the covariance matrix（共分散P）
2. Calculate the sigma points
Cholesky Decomposition（コレスキー分解）を計算するため、chol function in Matlab, or the Cholesky function in NumPyを利⽤する。
The parameter is a tuning parameter

## Slide 57: The Unscented Transform | Transforming and Recombining
Next we pass each of our 2N + 1 sigma points through the nonlinear function h(x)
yi = h(xi) i = 0, …, 2N
And finally compute the mean and covariance of the output PDF
2N
μy = ∑ αiyi
i=0
Mean:
Covariance:
2N
Σyy = ∑ αi (yi − μy) (yi − μy)
i=0
T
Weights:
αi =
κ
N + κ
1
2 (N + κ)
i = 0
otherwise

## Slide 58: The Unscented Transform vs. Linearization
1.01
1.00
0.99
0.98
y0.97
0.96
0.95
0.94
0.93
—0.4 —0.2 0.0 0.2 0.4
x
1.01
1.00
0.99
0.98
y0.97
0.96
0.95
0.94
0.93
—0.4 —0.2 0.0 0.2 0.4
x
1.01
1.00
0.99
0.98
y0.97
0.96
0.95
0.94
0.93
—0.4 —0.2 0.0 0.2 0.4
x
—0.4
—0.2
0.2
0.4
0.0
x
0.93
0.94
0.95
0.96
0.97
0.98
0.99
1.00
1.01
y
1.9
1.8
1.7
1.6
✓
1.5
1.4
1.3
1.2
0.985 0.990 0.995 1.000 1.005 1.010 1.015
r
0.985 0.990 0.995 1.000 1.005 1.010 1.015
r
1.2
1.3
1.4
1.5
1.6
1.7
1.8
1.9
✓
Cartesian coordinates
Polar coordinates
x = r cos θ y = r sin θ
Nonlinear transformation
Let’s revisit our nonlinear transformation example from the previous video.
True
Unscented transform
sigma points
True
Unscented
Linearized
The Unscented Transform gives a much better approximation for similar work!

## Slide 59: The Unscented Kalman Filter (UKF)
We can easily use the Unscented Transform in our Kalman Filtering framework with nonlinear models:
Nonlinear motion model
xk = fk−1(xk−1, uk−1, wk−1) wk ∼ 𝒩(0, Qk)
Nonlinear measurement model
yk = hk(xk, vk)
vk ∼ 𝒩(0, Rk)
Instead of approximating the system equations by linearizing, we will calculate sigma points and use the Unscented Transform to approximate the PDFs directly!
２つ非線形モデルなので、Unscented Transformも2回行う。

## Slide 60: UKF | Prediction step
To propagate the state from time (k – 1) to time k, apply the Unscented Transform using the current best guess for the mean and covariance
1. Compute sigma points
k−1
L̂k−1L̂T = P̂k−1
k−1
x̂(0) = x̂k−1
x̂(i)
k−1
= x̂k−1 +
i = 1...N
i = 1...N
k−1
x̂(i+N) = x̂k−1 −
N + κ coliL̂k−1
N + κ coliL̂k−1
2. Propagate sigma points
xˇ(i) = fk−1(x̂(i) , uk−1, 0)
k k−1
i = 0...2N
3. Compute predicted mean and covariance
α(i) =
κ
N + κ
1 1
2 N + κ
2N
i = 0
otherwise
ˇ
x
k
∑
= α xˇ
(i) (i)
k
i=0 2N
ˇ
P
k
∑
i=0
= α
(i)
( k
xˇ(i) − xˇ
k) ( k
k)
T
xˇ(i) − xˇ + Q
k−1
Additive process noise!
共分散の計算も理論的な式じゃなくて、統計学的な方法で計算していると思う。

## Slide 61: UKF | Correction step
To correct the state estimate using measurements at time k, use the nonlinear measurement model and the sigma points from the prediction step to predict the measurements
Additive measurement noise!
2. Estimate mean and covariance of predicted measurements
ŷk =
2N
∑
α(i)ŷ(i)
k
y
i=0 2N
∑
i=0
P = α
(i)
( k
ŷ(i) − y
k) ( k
̂
̂ ŷ(i) − y
k)
T
+ R
k
xy
3. Compute cross-covariance and Kalman gain
2N
∑
i=0
P = α
(i)
( k k) ( k
̂
xˇ(i) − xˇ ŷ(i) − y
k)
T
Kk = P P−1
xy y
̂ ˇ
T
4. Compute corrected mean and covariance
x̂k = xˇk + Kk (yk − ŷk)
Pk = Pk − KkPyKk
1. Predict measurements from (redrawn) propagated sigma points
k
k k
ŷ(i) = h (xˇ(i), 0) i = 0, …, 2N
With process noise considered!
To compute the Kalman gain, need the cross-covariance between the predicted state and the predicted measurements, which tells how the measurements are correlated with the state.
Sigma pointsは常にコレスキ分解で取らないといけない！Prediction stepで伝播した結果を使ってはいけません！
Step 4だけで測量値を使っている。

## Slide 62: UKF | Short example
Position
Height
p
x = [p· ]
··
u = p
ϕ
p
D
S
Motion/Process model
xk = f(xk−1, uk−1, wk−1)
= tan−1
yk = ϕk = h(pk, vk)
S
( D − pk )
+ v
k
wk ∼ 𝒩(0, (0.1)12×2)
Noise densities
vk ∼ 𝒩(0, 0.01)
Landmark measurement model
S and D are known in advance
= 1 Δt xk−1 + 0
[0 1 ] [Δt]
uk−1 + wk−1

## Slide 63: UKF | Short example
Data
x̂0 ∼ 𝒩
([5] [
0 , 0.01 0
0
1])
Δt = 0.5s
u0 = − 2 [m/s2]
S = 20 [m]
y1 = π/6 [rad]
D = 40 [m]
Using the Unscented Kalman Filter equations, what is our updated position?
p̂1
Position
Height
ϕ
p
D
S

## Slide 64: UKF | Short Example Solution
0
0
̂
L̂ L̂T = P
0
0
x̂(0) = x̂0
̂
(i)
0
x = x̂
0
i = 1 …, N
i = 1, …, N
0
x̂(i+N) = x̂0 −
+ N + κ coliL̂0
N + κ coliL̂0
0.1 0 0.1 0 T
[ 0 1] [ 0 1]
= [
0.01 0
0
1]
0
x̂(0) = 0
[5]
0
[5]
x̂(1) = 0 +
3 0.1 = 0.17
5
[ 0 ] [ ]
0
[5]
[1]
x̂(2) = 0 + 3 0 =
0
[6.73]
0
[5]
x̂(3) = 0 −
[ 0 ] [
3 0.1 = −0.17
5
]
0
[5]
[1]
x̂(4) = 0 − 3 0 =
0
[3.27]
Prediction
N = 2, κ = 3 − N = 1
Motion modelのsigma pointsを選択する
初期共分散をコレスキ分解する

## Slide 65: UKF | Short Example Solution
xˇ(i) = f0(x̂(i), u0, 0) i = 0,…, 2N
1 0
1
xˇ(0) =
[0 1 ] [5]
+
1 0.5 0 0
[0.5]
(−2) =
2.5
[ 4 ]
1
xˇ(1) = 1 0.5
[0 1 ] [
5
]
0.17 + 0
[0.5]
(−2) = 2.67
4
[ ]
1
[0
xˇ(2) = 1 0.5 0
1 ] [6.73]
+
0
[0.5]
(−2) = 3.37
[5.73]
xˇ
(3)
1
= 1 0.5
[0 1 ] [
−0.17 + 0
(−2) = 2.33
5 [0.5] 4
] [ ]
1
[0
xˇ(4) = 1 0.5 0
1 ] [3.27]
+
0
[0.5]
(−2) = 1.63
[2.27]
α(i) =
κ = 1 = 1
N + κ 2 + 1 3
1 1 1 1 1
i = 0
otherwise
2 N + κ = 2 2 + 1 = 6
xˇk =
2N
∑
i=0
α(i)xˇ(i)
k
3 [ 4 ] 6 [
4 6 [5.73] 4 6 [2.27]
= 1 2.5 + 1 2.67 + 1 3.37 + 1 2.33 + 1 1.63 = 2.5
] 6 [ ] [ 4 ]
Prediction
非線形Motion modelをsigma pointsに適用（この例では線形Motion modelを使っているけど）
非線形Transform後サンプルの平均値を計算する、予測値として使う

## Slide 66: UKF | Short Example Solution
ˇ
P
k
2N
∑
i=0
= α
(i)
xˇ(i) − xˇ
( k k) ( k
k)
T
xˇ(i) − xˇ + Q
k−1
= 1
2.5 − 2.5
2.5 − 2.5
3 ([ 4 ] [ 4 ]) ([ 4 ] [ 4 ])
T
+
1
6 ([
4
2.33 − 2.5
] [ 4 ]) ([
4
2.33 − 2.5
] [ 4 ])
T
+ 1
6 ([2.27]
1.63 − 2.5
[ 4 ]) ([2.27]
1.63 − 2.5
[ 4 ])
T
[ 0
+ 0.1 0
0.1]
= 0.36 0.5
[ 0.5 1.1]
This is the same result as in the linear Kalman Filter example because the motion model is already linear!
1
6 ([
4 4
2.67 − 2.5 2.67 − 2.5
] [ 4 ]) ([ ] [ 4 ])
T
+ 1
6 ([5.73]
3.37 − 2.5
[ 4 ]) ([5.73]
3.37 − 2.5
[ 4 ])
T
+
Prediction
非線形Transform後サンプルの分散を計算する

## Slide 67: UKF | Short Example Solution
1
1 1
y(̂ i) = h (xˇ(i),0)
i = 0,…, 2N
y(̂ 0)
1 = tan
−1
20
1
y(̂ 1) = tan−1
( 40 − 2.5 ) = 0.49
20
( 40 − 3.54 )
= 0.50
1
y(̂ 2) = tan−1
20
( 40 − 2.5 )
= 0.49
1
y(̂ 3) = tan−1
20
( 40 − 1.46 )
= 0.48
1
y(̂ 4) = tan−1
20
( 40 − 2.5 )
= 0.49
k
Lˇ kLˇ T = Pˇk
[0.83 0.64] [0.83 0.64]
0.60 0 0.60 0 T = 0.36 0.5
[ 0.5 1.1]
Redrawn sigma points!
(0)
xˇ1
2.5
= [ 4 ]
1
[ 4 ]
xˇ(1) = 2.5 +
3 0.60 = 3.54
[0.83]
0
[0.64]
[5.44]
2.5
[5.10]
1
[ 4 ]
xˇ(2) = 2.5 + 3
=
1
[ 4 ]
xˇ(3) = 2.5 −
3 0.60 = 1.46
[0.83]
0
[0.64]
[2.56]
2.5
[2.90]
1
[ 4 ]
xˇ(4) = 2.5 − 3
=
Correction
Measurement modelのsigma pointsを選択する。Motion modelでsigma pointsを変換した結果を使ってはいけません。違う分散をコレスキ分解するから。
Sigma pointsを非線形Measurement modelで変換する

## Slide 68: UKF | Short Example Solution
y
2N
∑
P = α
(i)
( 1 k) ( 1
y(̂ i) − ŷ y(̂ i) − ŷ
k)
T
i=0
= 1 (0.49 − 0.49)2 + 1 (0.50 − 0.49)2 + 1 (0.49 − 0.49)2 + 1 (0.48 − 0.49)2 + 1 (0.49 − 0.49)2 + 0.01
3 6 6 6 6
= 0.01
+ R
k
y1̂ =
∑
α(i)y(̂ i)
1
i=0
= 1 (0.49) + 1 (0.50) + 1 (0.49) + 1 (0.48) + 1 (0.49)
3 6 6 6 6
= 0.49
Correction
2N
変換後Sigma pointsの平均値や分散を計算する

## Slide 69: UKF | Short Example Solution
xy
∑
i=0
P = α
(i)
Correction
2N
( k k) ( 1
xˇ(i) − xˇ y(̂ i) − ŷ
k)
T
K
1
= P P
−1
xy y
=
0.004 1 = 0.40
[0.006] 0.01 [0.55]
1 1 1 1 1
[ 4 ]
[0.55] [4.02]
x̂ = xˇ + K (y − ŷ ) = 2.5 + 0.40 (0.52 − 0.49) = 2.51 =
p̂1
[p·̂1]
= 1
2.5 − 2.5
3 ([ 4 ] [ 4 ])
(0.49 − 0.49) + 1
6 ([5.44]
3.54 − 2.5
[ 4 ])
(0.50 − 0.49) + 1
6 ([5.10]
2.5 − 2.5
[ 4 ])
(0.49 − 0.49)
+ 1
6 ([2.56]
1.46 − 2.5
[ 4 ])
(0.48 − 0.49) + 1
6 ([2.90]
2.5 − 2.5
[ 4 ])
(0.49 − 0.49)
0.004
= [0.006]
X, y共分散の計算、gain matrixの計算、予測値の補正

## Slide 70: Summary | Unscented Kalman Filter (UKF)
The UKF uses the unscented transform to adapt the Kalman filter to nonlinear systems.
The unscented transform works by passing a small set of carefully chosen samples（sigma points） through a nonlinear system, and computing the mean and covariance of the outputs.
The unscented transform does a better job of approximating the output distribution than analytical local linearization, for similar computational cost.

## Slide 71: Summary | Kalman Filtering
The Kalman filter (KF) is a form of recursive least-squares estimation that allows us to combine information from a motion model and sensor measurements.
The KF uses the motion model to make predictions of the state, and uses the measurements to make corrections to the predictions.
The KF is the Best Linear Unbiased Estimator (BLUE).
1. Prediction
𝒩(xk̂ −1, P̂k−1)
PDF
Position (x)
𝒩(xˇk, Pˇk)
𝒩(yk, Rk)
𝒩(xk̂ , P̂k)
3. Correction
2. Measurement

## Slide 72: Summary | Nonlinear Kalman Filtering
EKF
ES-EKF
UKF
Unscented Transform
Best
Not required Slightly slower
Operating Principle
Linearization (Full State)
Linearization (Error State)
Accuracy
Good
Better
Jacobians
Required
Required
Speed
Slightly faster
Slightly faster
Because of UKF’s accuracy and simplicity, recommend using the UKF over the EKF whenever possible in projects.