## Slide 1: The Requirements for Autonomy
Module 1
1

## Slide 2: In this module ...
Taxonomy（分類学） of driving automation
Requirements for perception
Driving decisions and actions

## Slide 3: Taxonomy of Driving Automation
Module 1, Lesson 1
1

## Slide 4: Terms and Definitions
Driving task
  Perceiving the environment
  Planning how to reach from point A to point B
  Controlling the vehicle
Operational Design Domain (ODD)
運用条件を決める。
The ODD constitutes the operating conditions under which a given system is designed to function.
例えば、どんな環境、時間（昼/夜）、道路（高速道路か）でシステムが安定で動 けるか。特にシステムの安全性に大事。なので、事前のODDの設計は大事。

## Slide 5: How to classify driving system automation?
Driver attention requirements（運転手の注意がどれ程必要か）
Driver action requirements（運転手の操作がどれ程必要か）
What exactly makes up a driving task?

## Slide 6: What makes up a driving task?
Lateral control - steering

## Slide 7: What makes up a driving task?
Lateral control - steering
Longitudinal control - braking, accelerating
7

## Slide 8: What makes up a driving task?
Lateral control - steering
Longitudinal control - braking, accelerating
Object and Event Detection and Response (OEDR): detection, reaction
8

## Slide 9: What makes up a driving task?
lateral control - steering
longitudinal control - braking, accelerating
object and event detection and response (OEDR): detection, reaction
planning
  long term (route)
  short term
例えばlane change, intersection crossing.
9

## Slide 10: What makes up a driving task?
lateral control - steering
longitudinal control - braking, accelerating
object and event detection and response (OEDR): detection, reaction
planning
  long term (route)
  short term
Miscellaneous（雑多）
signaling with indicators. ウィンカー

## Slide 11: Autonomous Capabilities
Automated lateral control?
Automated longitudinal control?
OEDR
  Automatic emergency response
  Driver supervision
Complete vs Restricted ODD
自動化レベルを決めるために参考する項目

## Slide 12: Level 0 - No Automation
Regular vehicles, no automation

## Slide 13: Level 1 - Driving Assistance
Lateral Control
Longitudinal Control
Either, but not both
Lane Keeping Assistance
  can help you stay in your lane, if you drift
Adaptive Cruise Control（クルーズコントロール）
  can control speed, driver has to steer
Examples

## Slide 14: Level 2 - Partial Driving Automation
Lateral Control
Longitudinal Control
Both
Examples
GM Super Cruise
Nissan ProPilot Assist
...

## Slide 15: Level 3 - Conditional Driving Automation
Lateral Control
Longitudinal Control
OEDR
Includes automated object and event detection and response
Examples
Audi A8 Sedan
...
in the case of failure the control must be taken up by the driver. This is a controversial level of automation as it is not always possible for an autonomy system to know when it is experiencing a failure.

## Slide 16: Level 4 - High Driving Automation
Lateral Control
Longitudinal Control
OEDR
Fallback
Handles emergencies autonomously, driver can entirely focus on other tasks.
フォールバック：システム設計において、障害が発生しても、必要最小限の機能を維持して処理を続けられるようにしようとする考え方のこと。
レベル４は完全に緊急事態を対応できるが、運転手自分で対応するのも可能。
Level 4 system can handle emergencies on their own but may still ask drivers to take over to avoid pulling over（路肩に寄せる） to the side of the road unnecessarily.
(fall 2018) only Waymo!
自動運転における「フォールバック 」とは、自動運転から運転の権限が運転者に 委譲（いじょう）されるまでの間、自動運転システムの機能を制限した状態で稼働させることを指す。

## Slide 17: Level 4 - High Driving Automation
1
Example
Lateral Control
Longitudinal Control
OEDR
Fallback
7

## Slide 18: Level 5 - Full Driving Automation
Lateral Control
Longitudinal Control
OEDR
Fallback
Unlimited ODD

## Slide 19: Limitations of this taxonomy
ODD and safety record are more important!
具体的なODDが含まれてないので、２つシステムが共 にlevel 4のADが実現できたと言っても、 ODD上の能力の差が大きい可能性もある。
It is possible for two car models to claim level 4 autonomy but have very different capabilities in ODDs.

## Slide 20: Summary
Basic definitions
Driving task
Taxonomy requirements
Levels of automation, taxonomy

## Slide 21
Module 1, Lesson 2
Requirements for Perception（認知）

## Slide 22: Roughly ...
Analyze ego motion & environment (perception)
Decide on and plan a maneuver (planning)
Input
Drive

## Slide 23: What is perception?
We want to make sense of the environment and ourselves
Two things:
o identification（識別）
o understanding motion（予測）
Why?
o to inform our driving decisions
the quality of being aware of things through the physical senses, especially sight.

## Slide 24: Goals for perception
Static objects
o Road and lane markings (on-road)

## Slide 25: Goals for perception
Static objects
  Road and lane markings (on-road)
  Curbs（縁石、えんせき） (off-road)
curbs define the boundaries within which we can drive.

## Slide 26: Goals for perception
Static objects
  Road and lane markings (on-road)
  Curbs (off-road)
  Traffic lights (off-road)

## Slide 27: Goals for perception
Static objects
  Road and lane markings (on-road)
  Curbs (off-road)
  Traffic lights (off-road)
  Road signs (off-road)

## Slide 28: Goals for perception
Static objects
  Road and lane markings (on-road)
  Curbs (off-road)
  Traffic lights (off-road)
  Road signs (off-road)
  Construction signs, obstructions（障害物）, and more (on-road)

## Slide 29: Goals for perception
Dynamic objects (on-road)
  Vehicles
    4 wheelers (cars, trucks …)

## Slide 30: Goals for perception
Dynamic objects (on-road)
  Vehicles
    4 wheelers (cars, trucks …)
    2 wheelers (motorbikes, bicycles, …)
16

## Slide 31: Goals for perception
Dynamic objects (on-road)
  Vehicles
    4 wheelers (cars, trucks …)
    2 wheelers (motorbikes, bicycles, …)
  Pedestrians

## Slide 32: Goals for perception
Ego localization
  Position
  Velocity, acceleration
  Orientation, angular motion

## Slide 33: Challenges to perception
Robust（壮健） detection and segmentation
Sensor uncertainty
Occlusion, reflection
Illumination（照明）, lens flare（レンズフレア）
Weather, precipitation（降水）
With more training data, our segmentation and detection models perform better and more robustly, but collecting and labeling data for all possible vehicle types, weather conditions, and road surfaces is a very expensive and time-consuming process.
These can confuse perception methods with ambiguous information that is challenging to resolve into accurate estimates of object locations. ambiguous: 曖昧。
レンズフレア (lens flare) は、カメラによって写真・映像を撮影する際に、極めて明るい光源がレンズに向けて当てられている時や、画角内に極めて明るい光源が存在する場合に生じる、暗部（あんぶ）への光の漏れである。

## Slide 34: Summary
Perception
Goals for perception
  Static and dynamic elements, prediction
  Ego localization
Challenges to perception
KITTI Vision Benchmark Suite: http://www.cvlibs.net/datasets/kitti/

## Slide 35: Driving Decisions and Actions（計画）
Module 1, Lesson 3

## Slide 36: Planning: Examples
Making decisions
  Long term
    How to navigate from New York to Los Angeles?
  Short term
    Can I change my lane to the lane right of me?
    Can I pass this intersection and join the left road?
  Immediate（即座、そくざ）
    Can I stay on track on this curved road?（今の速度でこのカーブを通れるか）
    Accelerate or brake, by how much?

## Slide 37: Example: Turning left at an intersection
Approaching an intersection to turn left.
Assume
o Intersection has traffic lights

## Slide 38: Example: Turning left at an intersection
Identify turning lane for left turn.

## Slide 39: Example: Turning left at an intersection
Identify turning lane for left turn.
Approach the intersection, decelerate smoothly to the stop line.

## Slide 40: Example: Turning left at an intersection
Identify turning lane for left turn.
Approach the intersection, decelerate smoothly to the stop line.
What if
  Vehicle enters turn lane?
  Pedestrians are crossing?

## Slide 41: Example: Turning left at an intersection
Identify turning lane for left turn.
Approach the intersection, decelerate smoothly to the stop line.
What if
  Vehicle enters turn lane?
  Pedestrians are crossing?
  There are cars behind you?

## Slide 42: Example: Turning left at an intersection
This was a simple maneuver（操縦、そうじゅう）, yet it takes 3-4 levels of decisions and control to execute
Consider how many rules would it take to drive
o safely
o efficiently
o following all listed traffic rules
o only follow those rules everyone else is following!…（誰も守っているルールのみ守る）
Driving decision making is complicated!

## Slide 43: Reactive（反応） Planning
What we just did was rule based planning
  Involved decision trees!
In reactive rule based planning, we have rules that take into account the current state of ego and other objects and give decisions.
Examples:
  If there is a pedestrian on the road, stop.
  If speed limit changes, adjust speed to match it.
current stateのみを考える。将来は考えない。

## Slide 44: Predictive Planning
Make predictions about other vehicles and how they are moving. Then use these predictions to inform our decisions.
Example:
  That car has been stopped for the last 10 seconds. It is going to be stopped for the next few seconds.
  Pedestrian is jaywalking. She will enter our lane by the time we reach her.
ジェイウォークは、歩行者が、適切な交差点以 外の場所、または交通規則を無視して交通量 のある道路を歩いたり、横断したりしたとき に発生します。
predictive planning is the predominant（優勢な） method for self-driving cars, as it greatly expands the scenarios a vehicle can handle safely.

## Slide 45: Summary
12
Long term, short term, immediate planning
Simple intersection "making a left turn" scenario
Driving is hard!
Reactive planning, predictive planning

## Slide 46: Module Summary
In this module,
  Basic autonomous driving terminology（用語）
  Taxonomy to characterize self-driving capabilities
  The driving task and the major components of driving: perception, planning and execution.
  The elements and agents in the environment we need to identify and track for perception.
  Planning with its different horizons, and looked at some decision making approaches.
driving task; ODD.
static objects; dynamic object; ego localization.
short term, long term, immediate.
Paper: [2008] Autonomous driving in urban environments: Boss and the Urban Challenge. discusses one of the very early mixed planning systems. It was also the winner of the DAPRA Urban Challenge. https://onlinelibrary.wiley.com/doi/epdf/10.1002/rob.20255
Paper: [2016] A Survey of Motion Planning and Control Techniques for Self-Driving Urban Vehicles
https://ieeexplore.ieee.org/abstract/document/7490340
自動運転エンジニアになるため に ： fluent in C++ and Python
machine learning experience
be a proud software engineer about the quality of the code that you’re writing and you will do well.