## Slide 1: Safety Assurance for Autonomous Vehicles
Module 3

## Slide 2: In this module ...
Autonomous vehicle crash reports（Uber人身事故）
Safety concepts
Hazard（危険） sources
Industry perspectives on safety
Safety frameworks for self driving

## Slide 3: Safety Assurance for Self Driving
Module 3, Lesson 1

## Slide 4: Examples of Automated Vehicle Crashes
Image Source: The Verge Based on NTSB Report (2018)
March 2018, Arizona

## Slide 5: Uber Crash
Source: The Verge

## Slide 6: Uber Crash: Multiple Things Gone Wrong
No real time checks on safety drivers
After the woman was detected on the road (6 sec before)
o first classified as unknown object
o then misclassified as a vehicle
o then a bicycle
1.3 sec before, Volvo(ボルボ) system tried to do emergency braking maneuver
o but Uber had disabled（無効にする） it for testing
(理由：it is not safe to have multiple collision avoidance systems operating simultaneously during testing)
in the end, the decision made by the autonomy software was to ignore the detections possibly because they were too unreliable
失敗した点（できなかったところ）：
the perception system to correctly identify the pedestrian with a bicycle;
the planning system to avoid the detective object even though its class was uncertain;
the lack of human or emergency braking backup.

## Slide 7: Basic Safety Terms
Harm
Safety - “absence of unreasonable risk of harm（不合理な障害リスク）”
Hazard - “potential source of unreasonable risk of harm”
Probability Severity
Risk

## Slide 8: Major Hazard Sources
Mechanical
Cyber
Electrical
Hardware
Software
Perception
Planning
Fallback
自動運転における「フォールバック 」とは、自動運転から運転の権限が運転者に 委譲（いじょう）されるまでの間、自動運転システムの機 能を制限した状態で稼働させることを指す。 多分フォールバックができるかどうかという ことでしょう。

## Slide 9: NHTSA: Safety Framework(12項目)
Systems engineering approach to safety
Autonomy Design
Testing & Crash Mitigation
Based on NHTSA: A Vision For Safety 2.0 (2017)

## Slide 10: NHTSA: Autonomy Design
HMI
ODD
OEDR
Fallback
Cybersecurity
Traffic Laws
HMIで表示すべき項目（ユーザーを知らせるべきこと）：
(whether all sensors are operational,
what the current motion plans are, which objects in the environment are affecting our driving behavior…)

## Slide 11: NHTSA: Testing & Crash Mitigation
Post crash
Consumer Ed
Data recording
Testing
Crashworthiness
クラッシュ・ワージネス（英: crashworthiness） とは、飛行機や車両など、特にヘリコプター において、衝突の衝撃から乗員の安全性を確 保する性能のことである。
simulation, close track testing, public road driving
Crashes remain a reality of public road driving and autonomy systems that can minimize crash energy and exceed passenger safety standards in terms of restraints, airbags, and crashworthiness should be the norm.
Entities engaging in testing or deployment should consider methods of returning ADSs to a safe state immediately after being involved in a crash.
https://www.nhtsa.gov/sites/nhtsa.dot.gov/files/documents/13069a-ads2.0_090617_v9a_tag.pdf

## Slide 12: Summary
Autonomous driving accidents
Safety terms - harm, risk, hazard, safety
Major hazard sources
NHTSA safety framework
NTSB’s Report on the 2018 Uber Crash: https://www.ntsb.gov/investigations/AccidentReports/Reports/HWY18MH010-prelim.pdf
non-mandatory safety guidelines for autonomous cars in the NHTSA - Automated Driving Systems: A Vision for Safety 2.0 report: https://www.nhtsa.gov/sites/nhtsa.dot.gov/files/documents/13069a-ads2.0_090617_v9a_tag.pdf

## Slide 13: Industry Methods for Safety Assurance & Testing
Module 3, Lesson 2

## Slide 14: Waymo Safety Perspective
Based on Waymo Safety Report (2017)
https://waymo.com/safety/

## Slide 15: Waymo: Safety Levels
Behavioral Safety
Crash Safety
Functional Safety
Operational Safety
Non collision
safety
(interfaces are usable, convenient, intuitive)
(backups and redundancies) - even if a fault or failure occurs, the car can switch to a secondary component or a backup process to minimize the severity of failures and return the vehicle to a safe state, continuing the drive if possible.
system designs that minimize the danger to people that may interact with the system in some way, first responders（ファースト・レスポンダーとは災害や事故が起きた際に 最初に対応する警察や消防隊員）, mechanics（メカニック、整備員）, hardware engineers…
https://storage.googleapis.com/sdc-prod/v1/safety-report/Safety%20Report%202018.pdf
p11
Behavioral safety refers to the driving decisions and behavior of our vehicles on the road.（自車の運転決定や行動が安全か）
Crash safety, or crashworthiness, refers to the ability of vehicles to protect passengers inside the vehicles through a variety of measures, ranging from a structural design that shields people inside, to features like seat restraints（シートベルト） and airbags that mitigate injury or prevent death. （クラッシュでも乗客を保護できるか）

## Slide 16: Waymo: Safety Processes
Identify hazard scenarios & potential mitigations
Use hazard assessment methods to define safety requirements
  Preliminary(予備的) hazard analysis (PHA)
  Fault tree
  Design Failure Modes & Effects Analyses
Conduct extensive testing to make sure safety requirements are met
(top down) フォルトツリー解析
(bottom up) assess the effects of small subsystem failures on the overall capabilities of the system
リスクアセスメント手法一覧：
https://thinkit.co.jp/cert/article/0607/11/1/table.htm
これまでのハザードまたは故障の経験、知識を、将来、危害やハザードを招くおそれのある事象の特定を行い、さらに現時点で与えられている生産活動、施設、製品、システムの条件下でそれらが発生する可能性を特定する手法である。PHAは開発プロジェクトの初期段階で、設計の詳細や操作手順について情報がほとんどない場合に一般的に用いられる。

## Slide 17: Waymo: Levels of testing to ensure safety
Simulation testing
o Test rigorously with simulation, thousands of variations, fuzzing of neighbouring vehicles
ファジングとは、ソフトウェアの不具合（とく に脆弱（ぜいじゃく）性を意図することが多 い）を発見するためのテスト手法の一つであ る。ファズ（英語: fuzz）（予測不可能な入 力データ）を与えることで意図的に例外を発 生させ、その例外の挙動を確認するという方 法を用いる。ファズテストと呼ばれることも ある。
Waymoへの好評：the most publicly visible and well-documented program
Simulation testing: on the order of 10 million miles of simulation per day
- mine all of their on-road experiences for challenging scenarios and perform systematic scenario fuzzing, which changes the position and velocity parameters of other vehicles and pedestrians randomly.
- useful for finding hard edge cases.

## Slide 18: Waymo: Levels of testing to ensure safety
Closed-course testing（テストコース）
  Follow 28 core + 19 additional scenario competencies on private test tracks
  Focus on four most common crashes:
    Rear-end(追突), intersection, road departure(車線逸脱、いつだつ), lane change
(84% crashes )

## Slide 19: Waymo: Levels of testing to ensure safety
Real-world driving
  Start with smaller fleet, expand steadily
  Already testing thousands of vehicles, with more on the way.
increase public confidence in the technology

## Slide 20: General Motors Safety Perspective
Based on GM Safety Report (2018)

## Slide 21: GM: Safety
Address all 12 elements of NHTSA Safety Framework
Iterative Design
Analyze
Build
Improve
Simulate
Control car production!
Drive
(Waymo relies on OEMs to design its vehicles and only discuss mechanical and electrical hazards related to its autonomy hardware. GM manufactures their cars entirely themselves and so can enforce a more integrated design with consistent quality standards throughout the self-driving hardware.)
Waymoより強いポイント

## Slide 22: GM: Safety
Safety through Comprehensive Risk Management and Deep Integration
o identify and address risks, validate solutions
o prioritize elimination of risks, not just mitigation（緩和だけじゃなく、リスクの排除を優先する）
All hardware, software systems meet
o self-set standards for performance, crash protection, reliability（信頼性、故障や障害などによるシステムの停止や機能不全の発生しにくさ）, serviceability（保守性、障害復旧やメンテナンスのしやすさ）, security, safety
Deep integrationはよくわからない

## Slide 23: GM: Safety Processes
Deductive（演繹的、えんえき） Analysis
  fault tree analysis
Inductive（帰納的、きのう） Analysis
  Design & Process FMEA
Exploratory（探索的） Analysis
  HAZOP: Hazard & Operability Study
通常状態からのズレ（設定の温度や濃度）が発生した場合にその原因と発生する結果の事象を特定する。
この3手法は「Safety Frameworks for Self Driving」で紹介する

## Slide 24: GM: Safety Thresholds
All GM vehicles are equipped with two key safety thresholds:
Fail safes（失敗しても安全） - There is redundant functionality (second controllers, backup systems etc) such that even if primary systems fail, the vehicle can stop normally
SOTIF - All critical functionalities are evaluated for unpredictable（予測不可能な） scenarios

## Slide 25: GM: Testing
Performance testing at different levels
Requirements validation of components, levels
Fault injection（注入） testing of safety critical functionality
Intrusive（侵入的） testing such as electromagnetic（電磁、でんじ） interference（干渉、かんしょう）, etc.
Durability testing and simulation based testing
Is it really possible to truly precisely assess whether an autonomous car is safe? Or at least safer than a human driver?

## Slide 26: Analytical vs Data Driven: Definitions
Analytical Safety
Ensuring the system works in theory and meets safety requirements found by hazard assessment
Data driven safety
Safety guarantee due to the fact that the system has performed autonomously without fail on the roads for a very large number of kms
- example: Space Shuttle（スペースシャトル ） programのanalytical failure rates
- results need to be validated through experience(data driven).
these desired failure rates can be tied to human level driving performance.

## Slide 27: Are autonomous cars safer?
Driving is still dangerous!
Car accidents are mostly caused due to human errors (NHTSA Report, 2015)
In US, on average
  1 fatal collision per 146 million（1億以上） km
  1 injury collision per 2.1 million km
  ~ 1 collision per 400,000 km
(90%) a lack of judgement, a failure of human perception
逆にhumans are also extremely good at driving, and indeed, the entire driving environment has been designed based on human perception and planning abilities.

## Slide 28: Are autonomous cars safer?
Consider California disengagement rates:
In 2017, Waymo had
  Driven 563,000 km autonomously in California
  63 disengagements
  1 disengagement every 9,000 km
In 2017, GM had
  Driven 210,000 km autonomously in California
  105 disengagements
  1 disengagement every 2,000 km
Disengagement: when either this autonomy software requests the driver to take over control or the safety driver feels the need to intervene（介入する）.
disengagement状況の分類：
- unwanted vehicle maneuvers
- perception discrepancy（食い違い、相違）
- hardware issue
- software issue
- behavior predictions
- reckless（無謀、むぼう: doing something dangerous and not worrying about the risks and the possible results） road user (1 case)

## Slide 29: The Dilemma
Question: How many miles (years) would autonomous vehicles have to be driven to demonstrate with 95% confidence their failure rate to within 20% of the true rate of 1 fatality per 146 million km?
Answer: ~400 years, with a fleet of 100 vehicles travelling all the time (total ~8 billion miles)
o [How Many Miles of Driving Would It Take to Demonstrate Autonomous Vehicle Reliability? (Kalra et al., 2016) ]

## Slide 30: Summary
Industry perspectives
  Waymo - 5 safety levels, processes, testing
  GM - iterative design, processes, testing
Data driven safety
  Disengagement rates and road testing requirements
Waymo Safety Report https://waymo.com/safety/
GM Safety Report https://www.gm.com/content/dam/company/docs/us/en/gmcom/gmsafetyreport.pdf
あとUber, FordのSafety Report

## Slide 31: Safety Frameworks for Self Driving
Module 3, Lesson 3

## Slide 32: In this lesson, we will cover
Generic Safety Frameworks
  Fault Trees, FMEA, HAZOP
Autonomous/Automotive Safety Frameworks
  Functional Safety, Safety of Intended Functionality

## Slide 33: Car crash
Generic Safety Frameworks
OR
Fault Tree Analysis
  Top down deductive failure analysis
  Boolean logic
Software Failure
Hardware Failure
Manufacturing
defects(欠陥、けっかん)
Bad code
Hacked!

## Slide 34: Probabilistic Fault Tree Analysis
Assign probabilities to fault “leaves”
Use logic gates to construct failure tree
OR
AND
P(A)
P(B)
P(B)
P(A)
P(A) + P(B)
P(A) ᐧ P(B)
- assign probabilities of occurrence per hour or per mile of operation

## Slide 35: Failure Mode and Effects Analyses (FMEA)
Bottom up process to identify all the effects of faults in a system
Failure Mode
Modes or ways in which a component of the system may fail
Effects Analysis
Analyzing effects of the failure modes on the operation of the system

## Slide 36: FMEA: Idea
Categorize failure modes by priority
  How serious（深刻さ） are their effects?: Severity(S)
  How frequently do they happen?: Occurrence(O)
  How easily can they be detected?: Detection(D)
Eliminate or reduce failures, starting with top priority

## Slide 37: FMEA: Steps
1
Create FMEA table
Discuss with field experts
2
List failure modes
For each root cause
4
Occurrence? (O)
3
For each failure mode
identify effects
Severity? (S)
For each prevention method
5
Detection? (D)
RPN = S ᐧ O ᐧ D
6
2. question the purpose of the system and list all failure possibilities
4. For each consequence, identify the possible root causes; for each root cause, assign Occurrence (O, 1~10)
5. identify all the ways in which the failure mode can be detected by operator, maintenance, inspection, or a fault detection system. overall mode detection likelihood before it can causes an effect, Detection (D, 1~10, 10: impossible to detect)

## Slide 38: FMEA: Example
Consider following failure mode
  System encounters gravel（砂利、じゃり）, controller failure
    Severity: physical crash (S=10)
    Occurrence: whenever construction encountered, out of ODD, so somewhat likely (O=4)
    Detection: can check status monitor to identify if this happens with certainty (D=10)
    Risk priority number (RPN) = 10x4x10 = 400
簡単に検知できる。簡単に検知できればDは小さいはず。 https://en.wikipedia.org/wiki/Failure_mode_and_effects_analysis

## Slide 39: FMEA: Example
Similarly there could be other failure modes, for example:
  Sign perception failure (RPN = 100)
  GPS synchronization failure (RPN=300)
  Incorrect motion prediction (RPN=150)
Final RPN List:
  Control failure
  GPS failure
  Motion prediction
  Sign perception

## Slide 40: HAZOP – a variation on FMEA
Hazard and operability（操作性） study (HAZOP)
Qualitative brainstorming process, needs “imagination”
Uses guide words to trigger brainstorming (guide wordsの例：not, more, less etc.)
Applied to complex 'processes'
o Sufficient design information is available, and not likely to change significantly
- HAZOP is more of a qualitative process as compared to FMEA (quantitative).
- HAZOP is often used earlier in the design process to guide the conceptual design phase.

## Slide 41: Automotive Safety Frameworks
ISO 26262 - Functional Safety Standard
ISO/PAR 21448.1 – Safety of the Intended Functionality
Functional Safety is defined as:
o safety due to absence of unreasonable risk
o only concerned about malfunctioning（故障） system
ISO 26262 defines Automotive Safety Integrity Levels (ASIL)
o ASIL-D most stringent, ASIL-A least stringent

## Slide 42
Functional Safety Process
Requirements Specification
Architectural design
Unit design & implementation
System Integration and V&V
Software Integration（統合） and testing
Unit testing
Design-phase verification
Design-phase verification
ISO 26262
Summary Functional Safety Assessment
Distinction between:
- Validation testing (Are we building the right product?)妥当性確認する
- ensure that the product actually meets the user’s needs and that the specifications were correct in the first place
ユーザー要望を満たせているか
- Verification testing (Are we building the product right?)検証する
- ensure that the product is being built according to the requirements and design specifications
設計通り実現しているか。

## Slide 43: Functional Safety Process
Requirements Specification
Architectural design
Unit design & implementation
System Integration and V&V
Software Integration and testing
Unit testing
Design-phase verification
Design-phase verification
ISO 26262
Summary Functional Safety Assessment
Hazard and Risk Assessment (HARA)
Identify（識別） faults
Identify scenarios
Assess risks
Define worst-case scenarios
(FMEA or HAZOP)
(ODD)
Main idea behind functional safety: focus on worst-case requirements and then implement hardware and software that can at least handle these worst-case requirements.

## Slide 44: Safety of the Intended Functionality (SOTIF)
ISO/PAS 21448.1
Failures due to performance limitations and misuse
  Sensor limitations
  Algorithm failures / insufficiencies
  User misuse – overload（過負荷）, confusion, overconfidence
Designed for level 0-2 autonomy
Extension of FuSa（機能安全の拡張）
  V-shaped process
  Employs HARA

## Slide 45: Summary
Simple analytic frameworks
o fault trees and probabilistic fault trees
  Failure modes and effects analysis
Functional safety frameworks
  FuSa HARA - safety requirements through risk analysis
  SOTIF – behavior risk assessment
FMEA (failure mode and effects analysis):
https://asq.org/quality-resources/fmea
Function Safety for Road Vehicles: ISO 26262-1:2018（システム、hardware and softwareに関する安全） https://www.iso.org/standard/68383.html
Road Vehicles - Safety of the intended functionality: ISO/PAS 21448:2019（limitations and misuse に関する安全） https://www.iso.org/standard/70939.html
RAND Corporation Report on Driving to Safety How many miles of driving would it take to demonstrate autonomous vehicle reliability? https://www.rand.org/pubs/research_reports/RR1478.html
Address hazards in:
- design
- implementation
- operation
Example, Difference from Aerospace:
In aerospace you have a pilot who is highly trained and essentially the automation does all the easy medium staff, pilot is still there for all the hard staff. In self-driving case, we want to essentially automate everything.
Many of us would have known family members or people who’ve had an accident whilst driving a car. That’s a bad thing but after that accident, your neighbor doesn’t necessarily get a better driver.
But with driverless cars in 20 years time, I’ll be able to get into driverless cars that have the benefit of all the miles the other driverless cars have ever driven, and we exactly don’t have that with humans.
So there’s so many reasons why we want to fix transports in cities and when you’re in a plane and you look down out of a window, look how much of the infrastructure that we have built on our nations is because we want to move stuff.

## Slide 46: Module Summary
Motivation for safety
Formal definitions for safety concepts
NHTSA safety recommendations, 2017
Waymo and GM safety perspectives
Analytical and data-driven assessment
Common safety assessment frameworks
12個安全項目