## Slide 1: MODULE 5 An Autonomous Vehicle State Estimator

## Slide 2: Module 5 | Putting It All Together
In this module…
Sensor fusion
Calibration
Sensor failures

## Slide 3: MODULE 5 LESSON 1 STATE ESTIMATION IN PRACTICE
例えば、sensor fusion and calibration, speed and accuracy requirements, localization failures, parts of the environment that are moving and changing around us.

## Slide 4: State Estimation with Multiple Sensors
Self-driving vehicles rely on data streams from many different sensors (cameras, IMUs, LIDAR, RADAR, GPS, etc.)
How can we combine information from all these sources?
We will discuss the sensor fusion problem in Lesson 2 and how we can use the EKF to do this

## Slide 5: Calibration
What do we need to know about our sensors and the vehicle to do sensor fusion?
  Sensor models, which may depend on car- specific parameters (e.g., wheel radius)
Relative poses between each sensor pair, so we can combine information in a common reference frame
Time offsets between sensor polling times, so we combine only synchronized information
These are all critical forms of calibration, which we will discuss in detail in Lesson 3

## Slide 6: Accuracy Requirements
How accurate does the estimator need to be for safe self-driving?
Typically less than a meter for highway lane keeping
  Less for driving in dense traffic
GPS accuracy is 1-5 meters in optimal conditions
  Need additional sensors!
1.8 m
3.0 m

## Slide 7: Speed Requirements
How fast do we need to update the vehicle state to ensure safe driving?
How much computation power does the vehicle have on-board?
How much power can our computing resources consume?
an update rate of 15Hz to 30Hz is a reasonable target for self-driving.

## Slide 8: Localization Failures
How can localization fail?
  Sensors fail or provide bad data (e.g., GPS in a tunnel)
  Estimation error (e.g., linearization error in the EKF)
  Large state uncertainty (e.g., relying on IMU for too long)
We will discuss strategies for coping with sensor failures in Lesson 4
GPS can have a difficult time coping with reflected signals in cities with a lot of tall buildings
The uncertainty in state grows as we propagate forward through the motion model and it only shrinks once we incorporate outside observations from LiDAR or GPS for example.

## Slide 9: Our Dynamic World
Many of the models we use in practice for sensors like LIDAR, RADAR, cameras, etc. assume that the world is static and unchanging
In reality, the world is always moving and changing
We need to account for this in our models, or find ways of ignoring objects that don’t fit our assumptions
例えば、Lidar点群で自車運動量を予測する時や単眼カメラで自車運動量を予測する時だと思う。

## Slide 10: Summary | State Estimation in Practice
Practical state estimation typically fuses data from multiple sensors
Calibration is important for correct sensor fusion
Estimation algorithms must be designed with speed and accuracy requirements in mind
Need to be able to cope with localization failures and environmental changes

## Slide 11: MODULE 5 LESSON 2 MULTISENSOR FUSION FOR STATE ESTIMATION

## Slide 12: Multisensor Fusion for State Estimation
ℱ
s
ℱ
n
By the end of this video, you will be able to…
Develop an error state extended Kalman Filter for estimating position, velocity and orientation using an IMU, GNSS sensor, and LIDAR.

## Slide 13: Why use GNSS with IMU & LIDAR?
Error dynamics are completely different and uncorrelated（無相関）
IMU provides ‘smoothing（平滑「へいかつ」化）’ of GNSS, fill-in during outages（供給停止） due to jamming（ジャミング、電波妨害） or maneuvering
  Wheel odometry is also possible (if only 2D position orientation is desired)
GNSS provides absolute positioning information to mitigate IMU drift（ドリフト）
LIDAR provides accurate local positioning within known maps and in sky obstructed（遮られた「さえぎる」） locations.
+
+
correlatedの意味：if one fails, is the other likely to fail as well.
Choose sensors that are complimentary(補足的) in nature.
High-rate smoother
Known mapsはDetailed Road Mapや過去の運転で作ったOccupancy Grid MapやLocalization Mapかもしれないと思う。 Occupancy Grid MapやLocalization MapはLidar点群から（orカメラ）作ったんだ（C1M2 p55, 56）。
Conversely, GNSS can tell LiDAR which map to use when localizing.
疑問：Known mapsは？

## Slide 14: Tightly versus Loosely Coupled
4
EKF Coupling
Tight Loose
GNSS/LIDAR
Measurement
Pseudo-ranges to satellites LIDAR point clouds
Position
Accuracy
(Potentially) Higher
(Potentially) Lower
Complexity
Higher
Lower
Loosely coupled: assume the raw data have already been preprocessed to produce a noisy position estimate.
Tightly couple: tedious（退屈な） to implement and requires a lot of tuning.
ゆるい

## Slide 15: Extended Kalman Filter | IMU + GNSS + LIDAR
IMU
Kalman Fusion
Position Observation
GNSS
Low rate
LIDAR
High rate
If GNSS/LIDAR available
IMU Only
Predicted
State xˇk
Motion Model
Corrected
State x̂k
Motion Modelの更新はcan happen hundreds of times a second.

## Slide 16: Some Preliminaries（準備、前置き）
xk =
Vehicle state consists of position, velocity and parametrization of orientation using a unit quaternion:
pk
vk
∈ R10
qk
Motion model input will consist of specific force and rotational rates from our IMU:
uk =
fk
[ωk]
∈ R6
a 3D position, a 3D velocity, and a 4D unit quaternion representing the orientation of the vehicle with respect to a navigation frame.
From accelerometer and gyroscope measurements.
For clarity, assume IMU measurements are unbiased.
復習：navigation frameはa frame that is fixed w.r.t. the ground. 2種類：NED frame & ENU frame.

## Slide 17: Motion Model
Position
k
k−1
k−1
p = p + Δtv +
2
Δt
2
(
ns k−1
C f + g)
vk = vk−1 + Δt (Cnsfk−1 + g)
qk = qk−1 ⊗ q(ωk−1Δt) = Ω (q(ωk−1Δt)) qk−1
Velocity
Ω
qw
([qv])
w
= q 1 +
v
v
v ×
0 −qT
[q −{q } ]
ns ns k−1
q(θ) =
sin | θ |
θ
| θ |
2
cos
| θ |
2
where…
C = C (q )
Orientation
Sensor frameからnavigation frameへ回転
keep track of the orientation of sensor frame w.r.t. the navigation frame. これはORB_SLAM2と同じだと思う。
the orientation change is measured in the local sensor frame.
Navigation frameは初期フレームのことかもしれないと思う。もしくは、初期フレームがnavigation frameに対するオリエンテーショ。

## Slide 18: Linearized Motion Model
measurement noise
Error Dynamics
δxk = Fk−1δxk−1 + Lk−1nk−1
Error State
δxk =
δpk
δvk
δϕk
∈ R9
3x1 rotation error
1 1Δt
0
0 1 −[Cns fk−1]×Δt
0 0 1
k−1
L =
0 0
1 0 0 1
[
σ2
acc
σ2
gyro
]
nk ∼ 𝒩 (0, Qk)
∼ 𝒩 0, Δt2
where…
Fk−1 =
is the 3 ×３
identity matrix
There are some advantages to representing the orientation error in the global or navigation frame, rather than in the local frame.
Motion Modelがstateに対するJacobian行列だ。EKFもError-State EKFも同じだ。
赤い枠内の計算よくわかっていない。0は位置とオリエンテーションが独立していると意味していると思う。
直感的に言うと、速度モデルが加速度計ノイズを含んでいる、Orientationモデルはgyroscopeノイズを含んでいる
1
Quaternionは常にglobal / navigationフレームでのオリエンテーションだから、その差もglobal / navigationフレームを参照するんだ。
4次元Quaternionの差が3次元になるのは、global / navigationフレームの3軸に回る角度だ（オイラー角）と考えれば分かれると思う。オイラー角で表しているだけだと思う。 https://en.wikipedia.org/wiki/Conversion_between_quaternions_and_Euler_angles

## Slide 19: Measurement Model | GNSS
ℱ
n
yk = h(xk) + νk
= Hkxk + νk = [1 0 0] xk + νk
= pk + νk
νk ∼ 𝒩(0, RGNSS)
use a very simple observation of the position, plus some additive Gaussian noise.

## Slide 20: Measurement Model | LIDAR
ℱ
n
Known map
yk = h(xk) + νk
= Hkxk + νk = [1 0 0] xk + νk
= pk + νk
νk ∼ 𝒩(0, RLIDAR)
ℱ
s
We’ve assumed that LIDAR and GNSS will supply position measurements in the same coordinate frame.
In a realistic implementation, the GNSS position estimates may serve as a way to select a known map against which the LIDAR data can then be compared.
疑問：known mapは？
Occupancy Grid MapやLocalization Mapはオンラインで作ると思うので、過去の運転で作ったOccupancy Grid MapやLocalization Mapのことかもしれない。

## Slide 21: EKF | IMU + GNSS + LIDAR
pˇk = pk−1
k−1
+ Δtv +
2
Δt
2
(
ns k−1
n
C f + g )
vˇk = vk−1 + Δt (Cnsfk−1 + gn)
qˇk = Ω (q(ωk−1Δt)) qk−1
xˇk =
pˇk
vˇk
qˇk
pk−1, vk−1, qk−1
can be either be corrected or uncorrected depending on whether or not there was a GNSS/LIDAR measurement at time step k - 1
Loop:
1. Update state with IMU inputs
loop every time an IMU measurement occurs.

## Slide 22: EKF | IMU + GNSS + LIDAR
Loop:
Update state with IMU inputs
Propagate uncertainty
Pˇ k = Fk−1Pk−1FT 1 + Lk−1Qk−1LT 1
k− k−
Can either be
P̂k−1 or Pˇ k−1
Accounting for whether or not the previous state was corrected or uncorrected.
At this point, if don’t have any GNSS or LIDAR measurements available, can repeat step one and two.

## Slide 23: EKF | IMU + GNSS + LIDAR
Loop:
Update state with IMU inputs
Propagate uncertainty
If GNSS or LIDAR position available:
  Compute Kalman gain
Kk = Pˇ kHT(HkPˇ kHT + R)−1
k k
One of RGNSS or RLIDAR

## Slide 24: EKF | IMU + GNSS + LIDAR
Loop:
Update state with IMU inputs
Propagate uncertainty
If GNSS or LIDAR position available:
  Compute Kalman Gain
  Compute error state
δxk = Kk(yk − pˇk)

## Slide 25: EKF | IMU + GNSS + LIDAR
Loop:
Update state with IMU inputs
Propagate uncertainty
If GNSS or LIDAR position available:
  Compute Kalman Gain
  Compute error state
  Correct predicted state
p̂k = pˇk + δpk
v̂k = vˇk + δvk
q̂k = q(δϕ) ⊗ qˇk
global orientation error

## Slide 26: EKF | IMU + GNSS + LIDAR
Loop:
Update state with IMU inputs
Propagate uncertainty
If GNSS or LIDAR position available:
  Compute Kalman Gain
  Compute error state
  Correct predicted state
  Computed corrected covariance
P̂k = (1 − KkHk)Pˇ k

## Slide 27: Summary | EKF for Vehicle State Estimation
We used a loosely coupled EKF to fuse GNSS with IMU and LIDAR measurements
Assumptions:
  LIDAR provides positions in the same reference frame as GNSS (possible)
  IMU has no biases (not realistic!)
  State initialization is provided (realistic)
  Our sensors are spatially and temporally aligned (somewhat realistic)
[2017] Quaternion kinematics for the error-state Kalman filter: https://arxiv.org/pdf/1711.02508.pdf
[2017] Advanced Vehicle State Estimation: A Tutorial and Comparative Study: https://www.sciencedirect.com/science/article/pii/S2405896317323674

## Slide 28: MODULE 5 LESSON 3 SENSOR CALIBRATION: A NECESSARY EVIL

## Slide 29: Calibration: A Necessary Evil
R
Intrinsic（内部） Calibration
v = ωR
Extrinsic(外部) Calibration
ℱ
L
ℱ
W
Temporal Calibration
Δt
LW
{C , r
LW
W
}
(single sensor)
deal with sensor specific parameters.
deal with how the sensors are positioned and oriented on the vehicle.
deal with time offset between different sensor measurements.
Another example of an intrinsic sensor parameter is the elevation angle of a scan line in a LiDAR sensor like the Velodyne.

## Slide 30: Intrinsic Sensor Calibration
R
v
ω
How can we determine the parameters of our sensor models?
v = ωR
Manufacturer specifications
Measure by hand
Estimate as part of the state
either on the fly or more commonly as a special calibration step before putting the sensors into operation.
メリット：this approach has the advantage of producing an accurate calibration that’s specific to the particular sensor and can also be formulated in a way that can handle the parameters varying slowly over time.
For example, if you continually estimate the radius of your tires, this could be a good way of detecting when you have a flat(パンクしたタイヤ).

## Slide 31: Calibration by Estimation
R
ω
v
Position, p
x =
p p·
R
u = p··
p· = v = ωR
Position / Wheel Rate Observations
vk ∼ 𝒩(0, Rk)
Motion Model
k
x =
[
0 1 0
0 0 1
]
1 Δt 0
x
k−1
+
[
0
Δt
]
k−1
u + w
k−1
wk ∼ 𝒩(0, Qk)
Stateの中にタイヤの半径を入れている
0
自分が追加した

## Slide 32: Extrinsic Sensor Calibration
How do we determine the relative poses of all the sensors?
CAD model
Measure by hand
Estimate as part of the state
{
LI
C , r
LI
I
}
Determine the relative poses of sensors usually with respect to the vehicle frame.
For example, the relative pose of IMU and LiDAR, so that the rates reported by the IMU are expressed in the same coordinate system as the LiDAR point clouds.
all of the sensor frames have been nicely laid out.
this is often difficult or impossible to do accurately since many sensors have the origin of their coordinate system inside the sensor itself.

## Slide 33: Temporal Calibration
LIDAR clock System clock
IMU clock
ΔtL,S
ΔtI,S
How do we determine the relative time delays of all the sensors?
Assume zero
Hardware synchronization
Estimate as part of the state
For example, if we get LiDAR scans at 15Hz and IMU readings at 200Hz, might want to pair each LiDAR scan with the IMU reading whose timestamp is the closest match.
But in reality, there’s an unknown delay between when the LiDAR or IMU actually records an observation and when it arrives at the computer.
use hardware timing signals to synchronize the sensors, but this is often an option only for more expensive sensor setups.
LIDAR clock, System clock, IMU clockが同期できたら、このtime delayは測れるが、同期できない場合は、データがSystemに到達する時間しか利用できないと思う。

## Slide 34: MODULE 5 LESSON 4 LOSS OF ONE OR MORE SENSORS

## Slide 35: Multiple Sensors are Essential
Source: GM/Cruise Safety Report

## Slide 36: Sensing Failures
ℱ
n
ℱ
s
GNSS and other external sensors can fail as a result of the environment, or weather.

## Slide 37: Sensors Measurement Ranges
Source: electrek.co
2016 Tesla Model S Autopilot Sensors
Most cars have long, medium, and short range sensing.
  short range sensors for parking and to ensure not to collide with nearby vehicles.
  medium range sensors help in pedestrian and cyclist detection and in lane keeping.
  long range sensors help detect and predict the motion of approaching distant obstacles.
If one of these fails, have to ensure that the safety of the car occupants or the people around us is not compromised. （センサーが失敗する場合、周りの車や人に傷つけないように）

## Slide 38: Redundant Systems: 777 PFC
The 777 operates on a triple redundancy（冗長「じょうちょう」化） principle.
All major systems, including the flight computer, have two backups, each with independent power and separate programming and specifications.
  separate programmingはちょっとすごい。同じバグを防げるのは分かっているが。どう⾔う意味？下の説明によると、hardwareのみseparateされるらしい。つまりsoftwareは同じ？で はsoftwareのバグが発⽣したら、ヤバイ。多分これはそもそも許されないこと。
Each of the flight computers has a different processor to ensure that a bug in the architecture itself doesn’t affect all three computers.
  例えばprocessorはそれぞれmicro-processor AMD 29050, MOTOROLA(モトローラ) 68040, INTEL(インテル) 80486.
If one of the computers fails or malfunctions, the 777 uses a consensus（コンセンサス、合意） algorithm to seamlessly（継ぎ目なく） switch to another one.

## Slide 39: Redundancy is Crucial | Lane keeping
https://www.youtube.com/watch?v=6QCF8tVqM3I